## Slide 1
3GPP TSG SA WG6#30
April 8th - 12th 2019, Newport Beach, California, USA
Source: | Samsung
Title: | Application architecture for enabling edge applications
Document for: | Discussion
Agenda Item: | 10.7
Work Item / Release: | FS_EDGEAPP
Abstract of the contribution: This document discusses an architecture principles and requirements to derive an application architecture for enabling edge applications.
S6-190567

## Slide 2: General principles for 3GPP edge computing
UE application portability
Edge application portability
Service differentiation by mobile subscription
Independent operation of edge computing platform
Support of regional edge network deployment
Integration with 3GPP network

## Slide 3: 1. UE Application portability
Principle
  The change of UE application logic compared to existing central cloud environment should be avoided unless more value added service is required
Internet
Cloud
UE APP 1
Edge Infra
Edge App 1
Edge App 2
Edge
Enabler
Server
Edge Enabler Client
Edge Network
Comm.
Processor
APP 1
UE APP 2
UPF
Discover, initiation of available edge applications
Configuration for UE application to discover the address(es) of edge application(s) hosted in edge computing platform
Requirements
  The application architecture shall allow Edge enabler client to provides a set of enabling functionalities (such as discovery/initiation/configuration of available edge applications including address discovery of edge applications) without any modification of UE application

## Slide 4: 2. Edge application portability
Principle
  The change of edge applications logic compared to existing central cloud environment should be avoided unless value added service is required.
  One edge application shall be able to run in multiple operators’ edge computing platforms or operator-agnostic edge computing service provider without any modification
3rd Application
Provider
Edge Infra
Edge App 1
Edge App 2
Edge
Enabler
Server
Operator A
(edge computing provider X)
Edge
API X
Edge App 1
3rd Party application provider wants to have a common set of edge API
Edge App 1
Edge Infra
Edge App 1
Edge App 2
Edge
Enabler
Server
Operator B
(edge computing provider Y)
Edge
API Y
Requirements
  The application architecture shall allow the edge application to run on edge computing environment without any modification.

## Slide 5: 3. Service differentiation by mobile subscription
Principle
  The mobile operator should be able to provider service differentiation (e.g. enable/disable the edge service) based on UE subscription or operator policy
UDM
UPF
Edge
Enabler
Edge Network Service Area
UPF
Internet
Edge Network
 | Use | Edge App | Location
UE1 | O | App1, App2 | All
UE2 | O | App1 | All
UE3 | O | App2 | East
UE4 | X | - | -
UE4
UE1
Edge
Enabler
The operator shall be able to authorize the use of edge service (or edge enabling function) based on subscription
Requirements
  The application architecture shall allow the mobile network operator to authenticate the UE and to authorize the use of edge service or edge applications based on subscription.

## Slide 6: 4. Independent operation of edge computing
Principle
  The Edge computing platform can be managed by edge service provider independent of the PLMN operator.
  There can be multiple edge service providers within a single PLMN operator network.
UE1
UE3
Edge Network B
UPF
Edge Network C
UE2
Edge app list
UPF
Edge
Enabler
Edge
Enabler
Edge Service Provider X
Edge Service Provider Y
Edge Network A
Edge app list
Edge
Enabler
UPF
Requirements
  The application architecture shall support the multiple edge service providers per PLMN operator network.
  The application architecture shall be able to configure the UE for selected or available edge service provider(s) within the PLMN operator network.

## Slide 7: 5. Regional edge network deployment
Principle
  To support various edge computing deployment scenarios (e.g. gradual service deployment, differential regional service, localized service, or multi-vendor edge computing solutions/providers), the edge network, where the edge computing service is supported, can be partially deployed in a PLMN.
PLMN Area
Edge Network Service Area A
Edge Network Service Area B
Edge Network Service Area C
Edge
Config
UE
Edge Network Configuration
Requirements
  The application architecture shall allow the PLMN network operator to deploy edge computing service platform per regional basis. The application architecture shall allow multiple edge networks within a single PLMN where one edge network is defined as a subarea (e.g. list of TAs or cells) in the PLMN coverage.
  The application architecture shall be able to configure the UE with the relevant edge network service areas.
  The application architecture shall allow the UE to identify its location in relation to the edge network service area.

## Slide 8: 6. Integration with 3GPP network
Principle
  To integrate value-added features developed or to be developed in 3GPP network (such as location service, QoS, AF traffic influence) with edge applications, the application architecture shall support the interworking with 3GPP network with existing capability exposure functions such as NEF and PCF.
Requirement
  The application architecture supports various sets of application programming interfaces (including APIs defined by external fora) for edge applications using existing or enhanced 3GPP core network capability exposure.
Edge
Enabler
Edge Network
Edge
API
Direct use of exposure functions
NEF
PCF
SMF
UDM
AMF
3GPP Core Network

## Slide 9: Architecture requirements
The application architecture shall allow Edge enabler client to provides a set of enabling functionalities (such as discovery/initiation/configuration of available edge applications including address discovery of edge applications) without any modification of UE application (for UE application portability)
The application architecture shall allow the edge application to run on edge computing environment without any modification. (for edge application portability)
The application architecture shall allow the mobile network operator to authenticate the UE and to authorize the use of edge service or edge applications based on subscription. (for edge service differentiation by mobile operator’s subscription)
The application architecture shall support the multiple edge service providers per PLMN operator network. The application architecture shall be able to configure the UE for selected or available edge service provider(s) within the PLMN operator network. (for independent of edge computing platform)
The application architecture shall allow the PLMN network operator to deploy edge computing service platform per regional basis. The application architecture shall allow multiple edge networks within a single PLMN where one edge network is defined as a subarea (e.g. list of TAs or cells) in the PLMN coverage. The application architecture shall be able to configure the UE with the relevant edge network service areas. The application architecture shall allow the UE to identify its location in relation to the edge network service area. (for Regional edge network)
The application architecture supports various application programming interfaces (including APIs defined by external fora) for edge applications using existing or enhanced 3GPP core network capability exposure. (for Integration with 3GPP network)

## Slide 10: Discussion for the application architecture
Edge enabler client in the UE
  To meet the architecture principle 1, instead of individual UE application performs the edge enabling function, the new edge enabler client is proposed in the UE.
Edge enabler server function
  To meet the architecture principle 2, 3 and 6, edge enabler server function is proposed
Edge network configuration function
  To meet the architecture principle 4 and 5, edge network configuration function is proposed
UE APP 1
Edge App 1
Edge App 2
Edge Enabler
Server Function
Edge Enabler Client
UE APP 2
Edge Network Configuration Function
3GPP Network
Interworking with 3GPP network
Exposure of API to edge applications
Discovery/initiation/configuration of edge applications
Provisioning of Edge Network configurations
Edge Network
Separation due to architecture principle 4 and 5
Instead of individual UE application, the proposed edge enabler client performs the edge enabling functions

## Slide 11: Proposed architecture
It is proposed to adapt the application architecture for enabling edge applications with the following functional entities:
  Edge enabler client in UE
  Edge enabler server function
  Edge network configuration function
UE APP 1
Edge App 1
Edge App 2
Edge Enabler
Server Function
Edge Enabler Client
UE APP 2
Edge Network Configuration Function
3GPP Network
Interworking with 3GPP network
Exposure of API to edge applications
Discovery/initiation/configuration of edge applications
Provisioning of Edge Network configurations