3GPP TSG-SA WG6 Meeting #38-e	S6-201050

e-meeting, 20th – 31st July 2020	(revision of)

Source:	Samsung

Title:	Clarification on UP path management event API

Spec:	3GPP TS 23.558

Agenda item:	7.5

Document for:	Approval

Contact:	Hyesung Kim <hs1207.kim@samsung.com>

1. Introduction

<Introduction part >

2. Reason for Change

This pCR clarifies the UP path management event API to be aligned with operations in TS 23.502 by adding information elements necessary for the Edge Enabler Server to determine the type of subscription and/or indication of AF acknowledgement to be expected. The current User plane path management event API subscribe request in clause 8.6.3 does not clarify how early/late notification can be applied or how to let SMF expect the AF acknowledgement for UP path configuration/activation.

Additionally, this pCR introduces the use of Nnef_APISupportCapability or Availability of service APIs event notifications to monitor and provide the availability of the UP path management event API.

3. Conclusions

4. Proposal

It is proposed to agree the following changes to 3GPP TS 23.558.

* * * First Change * * * *

<Proposed change in revision marks>

#### 8.6.3.2	User plane path management event API

Figure 8.6.3.2-1 illustrates the subscribe/unsubscribe operation between the Edge Application Server and the Edge Enabler Server for user plane path management event notifications.

Figure 8.6.3.2-1: User plane path management event API: Subscribe/Unsubscribe Operation

1.	The Edge Application Server requests user plane path management event subscribe operation for tracking the UE's user plane path change continuously. The Edge Application Server shall include UE Identifier. For cancelling the subscription, the Edge Application Server uses the unsubscribe operation.

If the request is subscribe, the Edge Application Server may include Subscription Type (Early and/or Late notification defined in 3GPP TS 23.501 5.6.7) and/or Indication of EAS Acknowledgement.

2.	If the request is subscribe, the Edge Enabler Server checks if the Edge Application Server is authorized for this operation. If authorized, Edge Enabler Server checks if there exists a subscription with the 3GPP core network for the user plane path management event notifications corresponding to the UE information obtained in step 1 as described in 3GPP TS 23.501 [2] and 3GPP TS 23.502 [3], which may be triggered by other Edge Application Server for the same UE. The Edge Enabler Server checks the availability of the user plane path management event service for the UE based on UE Identifier and UE Registration Mode (S1 and/or N1).

a.	if a subscription with 3GPP core network does not exist, then the Edge Enabler Server subscribes with the 3GPP core network (PCF, NEF or SCEF+NEF) for the user plane path management event notifications of the UE as described in 3GPP TS 23.501 [2] and 3GPP TS 23.502 [3]. If the Edge Application Server provides Subscription Type and/or Indication of EES Acknowledgement, the Edge Enabler Server include the type of subscription the indication of “AF acknowledgement to be expected” as information on AF subscription to corresponding SMF events within the AF Request;

b.	if a subscription with 3GPP core network exists, then the Edge Enabler Server uses the locally cached user plane path management event notification information of the UE to respond to the Edge Application Server.

The Edge Enabler Server stores the subscription related to the Edge Application Server.

If the request is unsubscribe, the Edge Enabler Server checks if the Edge Application Server is authorized for this operation and if authorized removes the subscription related to the Edge Application Server.

3.	If Edge Application Server is authorized, the Edge Enabler Server responds with a subscription information for the subscribe request. If Edge Application Server is not authorized, the Edge Enabler Server provides a rejection response with cause information. If the request is for unsubscribe, the Edge Enabler server provides an ACK response for the unsubscribe request.

If the target UE and the 3GPP network support mobility between 5GC and EPC, the Edge Enabler Server monitors the availability of the user plane path management event notification from the 3GPP network by utilizing Nnef_APISupportCapability or Availability of service APIs event notifications provided by the CAPIF core function. The Edge Enabler Server is aware of the mobility capability of the 3GPP network based on the local configuration and obtains UE capability of mobility between 5GC and EPC via the Edge Enabler Client.

Figure 8.6.3.2-2 illustrates the notify operation between the Edge Enabler Server and the Edge Application Server for continuous User plane path management event notifications.

Figure 8.6.3.2-2: User plane path management event API: Notify Operation

1.	The Edge Enabler Server detects the user plane path management event of the UE (e.g. receiving User plane path management event notification for the UE from the 3GPP core network). The Edge Enabler Server may cache the detected User plane path management event notification locally with timestamp as the latest information of the UE. The Edge Enabler Server determines to notify the user plane path management event notification information (e.g., DNAI) to the Edge Application Servers which has subscribed for the user plane path management event.

2.	The Edge Enabler Server sends user plane path management event notify operation to the Edge Application Server. The Edge Enabler Server includes the user plane path management event notification information of the UE and optionally the timestamp. The timestamp can be included to indicate the age of the user plane path management event notification information. The Edge Enabler Server may only provide part of information included in the user plane path management event notification from 3GPP network (e.g. DNAI). If the Edge Enabler Server had provided indication of “AF acknowledgement to be expected” to 3GPP network as in clause 4.3 of 3GPP TS 23.502, the Edge Enabler Server waits for acknowledgement from the EAS before it sends AF acknowledgement to the 3GPP core network.

* * * Next Change * * * *

#### 8.6.3.3	Information flows

##### 8.6.3.3.1	User plane path management event API subscribe request

Table 8.6.3.3.1-1 describes the information elements for a User Plane Path Management Event API Subscribe Request from the Edge Application Server to the Edge Enabler Server.

Table 8.6.3.3.1-1: User plane path management event API subscribe request

| Information element | Status | Description |
| --- | --- | --- |
| UE Identifier | M | The identifier of the UE (i.e. GPSI or identity token) |
| Event ID(s) | M | Event ID(s) as specified in 3GPP TS 23.501 [2] |
| Event Report | M | Event Reporting Information as specified in 3GPP TS 23.502 [3] |
| Notification Target Address | M | Notification Target Address of the EAS where the notification is to be sent by the EES |
| Type of subscription | O | Indicates Early and/or Late notification to inform if the notification needs to be received before and/or after UP path configuration. |
| Indication of EAS acknowledgement | O | This IE indicates the EES to include indication of “AF acknowledgement to be expected” within the AF request for subscribing UP path management events to 3GPP network and that the EAS will provide an acknowledgement as a response for the notifications of UP path management events to the EES. |
| Event Filter | O | Event filter as specified in 3GPP TS 23.501 [2] |

Editor's note:	The detailed applicable information in "Event Report" is FFS.

##### 8.6.3.3.2	User plane path management event API subscribe response

Table 8.6.3.3.2-1 describes the information elements for a User Plane Path Management Event API Subscribe Response from the Edge Enabler Server to the Edge Application Server.

Table 8.6.3.3.2-1: User plane path management event API subscribe response

| Information element | Status | Description |
| --- | --- | --- |
| Result | M | Indicates whether the subscription is successful or failure |
| Cause information (see NOTE 1) | O | Indicates the cause information for subscription failure |
| Subscription ID (see NOTE 2) | O | Subscription identifier corresponding to the subscription stored in the EES for the request |
| Expiry time (see NOTE 2, NOTE 3) | O | The expiry time of the subscription |
| NOTE 1: The Cause information IE is included when the Result indicates failure. NOTE 2: The Subscription ID IE and Expiry time IE are included when the Result indicates success. NOTE 3: The Expiry time IE if not included indicates that the subscription never expires. |

* * * End of Change * * * *