3GPP TSG-SA WG6 Meeting #38-e	S6-201143

e-meeting, 20th – 31st July  2020	(revision of S6-20xxxx)

Source:	Huawei, Hisilicon

Title:	Update EES profile with service area information of EDN

Spec:	3GPP TS 23.558 v0.3.0

Agenda item:	7.5

Document for:	Approval

Contact:	Cuili Ge (gecuili@huawei.com), Niranth (namogh@huawei.com)

1. Introduction

This pCR proposes to include EDN service area information for the EES.

2. Reason for Change

According to the deployment options and the previous discussion on EES service area, this pCR proposes to use the LADN service area or a list of DNAI(s) which is associated with the EDN where the EES is located, to describe the “service area” of the EES.

3. Proposal

It is proposed to agree the following changes to 3GPP TS 23.558 v0.3.0.

* * * First Change * * * *

### 8.2.6	Edge Enabler Server Profile

The Edge Enabler Server profile includes information about the EES and the services it provides.

Table 8.2.6-1: Edge Enabler Server Profile

| Information element | Status | Description |
| --- | --- | --- |
| EES ID | M | The identifier of the EES |
| EES Endpoint | M | Endpoint information (e.g. URI, FQDN, IP address) used to communicate with the EES. This information is provided to the EEC to connect to the EES. |
| Edge Application Server Profiles | M | List of Edge Application Servers registered with the EES. |
| EES Provider Identifier | O | The identifier of the EES Provider (such as ECSP) |
| A list of DNAI(s) | O | The list of DNAIs which is associated with the EES |

Editor's Note: The subset of EAS information provided by the EES is FFS.

Editor's Note: Whether there is a need to specify a Service Area for the EES is FFS.