## Slide 1: SA6#45-e, S6-211933, Discussion Paper Motivation for CR S6-211882 Rev-1 of S6-211519 Enhancements for MC service UE label TS 23.280 V17.7.0
Andreas Platzer, BDBOS
18th August 2021

## Slide 2: Dependency to SA6#44-e
CR S6-211882, is written on top of
S6-211519, Rev-0, “Clarifications for Location management”, which is not yet incorporated in TS 23.280, but agreed at SA6#44-e.
Rev-1 adds new parts for “MC service UE label”.
  All changes from Rev-0 are still visible.
  New added text in Rev-1 is highlighted in .
Yellow

## Slide 3: Motivation, History and Goal
Motivation
Main reason for “MC service UE label” is to allow a e.g. dispatcher to distinguish MC service UEs, when an MC service user has logged into multiple UEs at the same time.
History of “MC service UE label”:
Introduced and agreed at SA6#42-e with S6-210581.
Additions, proposed at SA6#42-bis-e with S6-211048 were postponed.
Goal for this meeting:
To provide a complete feature within Rel-17, only necessary enhancements for “MC service UE label” are proposed.

## Slide 4: Content of S6-211882 was 211519
“MC service UE label” is added in identified information flows.
Procedures, related to location information, are updated to handle “MC service UE label”.
  The location management server shall STORE the “MC service UE label”. (Allowing location history procedures to provide “MC service UE label”).
  Added as Note: The MC service server needs NOT to be informed about the “MC service UE label” (as it has no use for it).

## Slide 5: 10.9.2.x Information flows for location information
LMS
LMC
10.9.2.2 Location information report
MC service server
LMC x
10.9.2.10 Location report response
10.9.2.7 Location information notification
10.9.2.14 Location information history report
10.9.2.14 Location information history report
Location provider
Location consumers
Location
information
Present, realized with S6-210581
This CR, S6-211882
10.9.2.2 Location information report

## Slide 6: Alternative solution
The „MC service UE label“ is sent and stored only to the Location management server.
Location management clients, interested in the „MC service UE label“ use new procedures to request the label explicitly.
Evaluation
  + avoid sending the “MC service UE label” together with each location information
  New procedures and new information flows needed
  Mapping of labels to existing location information needed.
This alternative solution is not pursued further.