## Slide 1: DP on the deployment, architecture, value of FS_NSCALE
CMCC , Huawei
3GPP TSG-SA WG6 SA6#45e

## Slide 2: Content
Slice enabler layer deployment
Value of SA6 FS_NSCALE work
Function model

## Slide 3: Slice enabler layer deployment
NSI #4
NSI #3
S-NSSAI #2
S-NSSAI #3
NSI #2
S-NSSAI #4
Verticals requirements
2B verticals have strong desires for self service and management for the slice and the service, including:
  Slice order and management including slice creation, update, termination
  Slice SLA monitoring
  Slice access control of UE/application service
  Service QoE monitoring
  …..
The value of slice enabler
Enable the MNO to provide the slice and the suite of tools, i.e., help vertical/enterprise to achieve self service and management in an efficient way;
Enable new and flexible slice operation business model
CSMF
NSMF
……
MNO
S-NSSAI #1
NSI #1
CN
…
PCF
UDM
AN
TN
Slice Enabler
Vertical/Enterprise #1
Vertical/Enterprise #..N
UE/client side
Server side
AGV control
Factory service
…
Slice Enabler
Deployment
The Slice Enabler Server/Client could be deployed at the vertical/enterprise domain and/or MNO domain, or both.

## Slide 4: Function Model
Network slice Capability Exposure client The network slice capability exposure client functional entity acts as the application client for the slice enablement. The network slice capability exposure client interacts with the network slice capability exposure server to trigger a network slice related operations. This trigger may be due to an application QoS requirement change, a service operation change, a network slice status change, etc.. The NSCE client may receive a network slice related notification from the NSCE server. The NSCE client may optionally notify the VAL client on the network slice / DNN change. The NSCE client could also provides and receives configuration data from the NSCE server.
Network slice Capability Exposure server The network slice capability exposure server functional entity provide application layer enablement to support the network slice management and control with/without invoking control and management plane capabilities from SA2 and SA5 pertaining to network slicing. Such enablement supports the network slice related operations such as the mapping or migration of one or more vertical applications to one or more network slices, triggering the dynamic network slice lifecycle management, NSI/NSSI monitoring, etc.

## Slide 5: Slice capabilities from SA2
Core network capability/Northbound API from SA2
URSP mechanism to manage the slice access control;
Slice quota management and event exposure with NSACF(network slice admission control function)
  Quota on the maximum number of UEs (Event can be exposed to 3rd AF)
  Quota on the maximum number of PDU Sessions (Event can be exposed to 3rd AF)
  Uplink/ Downlink throughput per UE
  Uplink/ Downlink throughput per network slice
Network data analytics from NWDAF
  Load level information on a network slice level
  Observed Service Experience for a Network Slice
  User Data Congestion Analytics per slice level
  Dispersion Analytics at a slice
  DN Performance Analytics

## Slide 6: Slice capabilities from SA5
Network Slice related Management Services defined by SA5
1） Network Slice Provisioning for both NSaaS and NoP model (TS 28.531)
Provisioning for NSI/ Provisioning exposure for NSI (This management service enables its consumer to request allocating, deallocating, or modifying an NSI.)
Provisioning data report for NSI/ Provisioning exposure data report for NSI (This management service enables its consumer to obtain notifications about NSI Information model data.)
2） Network Slice Performance Assurance (TS 28.550)
Measurement job control services
NSI performance data file reporting service
NSI performance data streaming service
3）Network Slice Fault Supervision (TS 28.545)
Fault supervision Data Report for NSI
Fault supervision Control for NSI
The Network slice management service exposure in SA5 can be seen as SCEF/NEF. In SA5,
  one aspect is about defining the MnS itself including operation and data model;
  the other aspects is the MnS access control (like the API discovery/API revocation access control at the CCF and AEF）, which is mainly the policy aspect
However, the ongoing part, access control policy is out of the SA6’s scope.
Notes: invisible

## Slide 7: Relationship and Value
SA6 Slice Enabler can directly re-expose SA5 and SA2 to enable the self service and management
SA6 Slice Enabler can further develop new service API with/without SA5/SA2 capability/service API to facilitate the vertical/enterprise better manage their service, e.g., service QoE monitoring.
SA6 may identity gaps which needs SA2/SA5 to develop new capabilities/service APIs. For example, dynamically switch particular UE(s)/application(s) from one slice/NSI to another slice/NSI on demand, which cannot be well satisfied by the existing OAM mechanism.

## Slide 8: Examples: Service QoE/Slice self monitoring
AGV APP
The Slice Enabler Server/Client, are deployed at the vertical/enterprise domain，are the assets of the vertical/enterprise and managed by themselves.
The Slice Enabler Server/Client is able to aggregate several domain’s input to achieve self monitoring, including:
  QoE metrics from the application layer domain (especially from the client side), the NWDAF may not be applicable as the data are local handled without routing outside the campus;
  QoS monitoring (UE-UPF) from the core network domain;
  Slice KPI monitoring from the management domain
optimized actions: Fault location
NSI #4
NSI #3
S-NSSAI #2
S-NSSAI #3
S-NSSAI #4
CSMF
NSMF
……
S-NSSAI #1
NSI #1
CN
UPF
PCF
UDM
AN
TN
Slice Enabler Server
UE/client side
Server side
FFAPP
NWDAF
…
Vertical/Enterprise Campus
MNO
domain
Slice Enabler Client
AGV AS
FF AS
UE
I: QoE monitoring & collection
I:QoE monitoring & collection
I:Slice KPI monitoring
I:QoS monitoring…
I:N6 measurement…
Output:
Visual Views