## Slide 1: 5GMARCH – Open Issues
Basavaraj (Basu)
Samsung

## Slide 2: 5GMARCH Open Issues
Issue-1: Non-MSGin5G UEs to initiate communication (p2p and group) towards MSGin5G service end points
Issue-2: Group information towards Non-MSGin5G UEs
Issue-3: Protocol adaptation when MSGin5G UEs support divergent protocols
Issue-4: Routing based on UE Service ID for message delivery to MSGin5G UEs and Non-MSGin5G UEs

## Slide 3: Issue-1: Non-MSGin5G UEs to initiate communication (p2p and group) towards MSGin5G service end points [1/2]
Examples from 3GPP TS 23.283
10.3.3.3 Group call setup initiated by LMR user on an interworking group defined in MCPTT system
Notes:
The interworking group has been defined in MCPTT system.
The mapping relationship of group and user identities between the MCPTT system and the LMR system has been configured at the IWF.
LMR user initiates a group call.
10.4.2.2 LMR user initiating a private call with MCPTT user
Notes:
The LMR user at the LMR system has initiated a private call towards an MCPTT user.

## Slide 4: Issue-1: Non-MSGin5G UEs to initiate communication (p2p and group) towards MSGin5G service end points [2/2]
More examples from 3GPP TS 23.283
10.8.7 LMR user one-to-one SDS request to an MCData user
10.8.7.1 Signalling control plane
The procedure for an IWF requesting, on behalf of an LMR user, to send a signalling control plane SDS to a single MCData user is as specified in 3GPP TS 23.282 [6] subclause 7.4.2.2 for the one‑to‑one standalone short data service using the signalling control plane, with the exception that MCData client 1 is located behind the IWF. The source address of the SDS is the MCData ID that has been allocated to the LMR user. The IWF behaves as a peer MCData server.
10.8.9 LMR user group SDS request to an MCData group
10.8.9.1 Signalling control plane
The procedure for an IWF requesting, on behalf of an LMR user, to send a signalling control plane SDS to an MCData group is as specified in 3GPP TS 23.282 [6] subclause 7.4.2.5 for the group standalone short data service using the signalling control plane, with the exception that MCData client 1 is located behind an IWF and one or more of the MCData clients 2 to n can be behind IWFs that have affiliated to the MCData group (see subclause 10.1.2 of the present document). The SDS is addressed to the MCData group ID. The IWF behaves as a peer MCData server to other MCData servers.
Proposal 1:
  To make progress, we are fine with the assumption that we do not support Non-MSGin5G UEs initiate communication (p2p and group) towards MSGin5G service end points in Rel-17. Based on the existing SA1 requirements, we could see this in the future release.
  Also this issue is independent of the discussion on why additional info (list of groups members, policy) apart from Group ID is required in the Group Notification towards Non-MSGin5G UEs.

## Slide 5: Issue-2: Group information towards Non-MSGin5G UEs
Proposal is revised to go with Approach 3
Notification should include – list of members, Group configuration
Justification:
  MC IWF supports IWF group information request/response procedures from the IWF to GMS (TS 23.283 Clause 10.2.3.3 IWF requests group configuration from the MC system)
  Instead of adding a new interface between Gateway and SEAL Servers and specifying a separate request/response procedure, it is simple to include list of members, Group configuration along with notifying Group Service ID
Proposal 2: To include list of members, Group configuration in the Group Notification along with Group ID.
List of members | M | List of VAL user IDs or VAL UE IDs that are part of the created group
Group Configuration | M | Group configuration information (NOTE)
NOTE: Group configuration information can be obtained independently by MSGin5G Server (VAL server) according to subclause 10.3.6.2 specified in 3GPP TS 23.434 [5]. |  | 

## Slide 6: Issue-3: Protocol adaptation when MSGin5G UEs support divergent protocols
MSGin5G Service is application layer service
MSGin5G Message defined in TS 23.554 – It needs to send leveraging some application level protocols
  E.g. #1: MSGin5G Message can be sent over HTTP
    As per RFC 7231: “The Hypertext Transfer Protocol (HTTP) is a stateless application-level protocol for distributed, collaborative, hypertext information systems.”
  E.g. #2: MSGin5G Message can be sent over CoAP
    As per RFC 7252: “The Constrained Application Protocol (CoAP) is a specialized web transfer protocol for use with constrained nodes … ”
  E.g. #3: any other protocol
  Actual selection of protocol using which the MSGin5G will be sent is CT1 responsibility
However, MSGin5G service needs to support both constrained device and unconstrained devices
If MSGin5G message is sent over HTTP by unconstrained MSGin5G UE towards constrained MSGin5G UE (which understands MSGin5G Message received over CoAP only)
  In this case, we need an entity who adapts from one application protocol to another.
Question :
  Do you think that MSGin5G UEs can support different Stage-3 protocols based on the understanding of our architecture which supports constrained and unconstrained devices?
Proposal 3:
  Proposal is to remove Clause 5.3.2.3 and replace it with a Architecture Requirement as discussed on the last SA6 conf call.

## Slide 7: Issue-4: Routing based on UE Service ID [1/2]
Issue: To determine next hop for message delivery towards MSGin5G UEs
As per our architecture:
  MSGin5G Service supports UE Service ID which could of a MSGin5G UE or Non-MSGin5G UE (Legacy 3GPP UE or Non-3GPP UE)
  All UEs expected to consume MSGin5G Service are required to perform registration at MSGin5G Server
  MSGin5G Server communicates to MSGin5G UEs and Non-MSGin5G UEs on different interfaces
For Messages (p2p or Group) that needs to be delivered to a MSGin5G UE:
  Based on UE Service ID of MSGin5G UE, the MSGin5G Server sends the message over MSGin5G-1 interface

## Slide 8: Issue-4: Routing based on UE Service ID [2/2]
As per our architecture:
  MSGin5G Service has multiple Message Gateways (Legacy 3GPP Message Gateway and Non-3GPP Message Gateway)
  Non-MSGin5G UEs register to the MSGin5G Server via Message Gateways
  MSGin5G Server communicates to Non-MSGin5G UEs on different interfaces (MSGin5G-2 or MSGin5G-4 )
For Messages (p2p or Group) that needs to be delivered to a Non-MSGin5G UE:
  The MSGin5G Server has to make a decision on whether to use MSGin5G-2 or MSGin5G-4 interface
  Hence, MSGin5G Server has to make a decision on selection of the appropriate Message Gateway (based on Non-MSGin5G UEs registration)
Questions to be addressed in the proposal for Routing:
  1. Is routing of non-MSG5G UE registration based on MSGin5G Server Service ID or MSGin5G Server address?
  2. Does MSGin5G Server store the mapping of Non-MSGin5G UEs and the Service ID of the corresponding Message Gateway during the Non-MSGin5G UE registration?
  3. If routing is based on UE Service ID and would be handled by the underlying layer then why do we need different interfaces MSGin5G-1, MSGin5G-2 and MSGin5G-4 in our architecture?

## Slide 9: Summary
It is requested to agree way forward as per the proposals made on the slides
It is requested to provide answers to questions posed on the slides