## Slide 1: Discussion Paper on the Deployment and Role of FS_NSCALE
JIA Xiaoqian
Huawei

## Slide 2: Outline
Challenges of Campus Network Management
Role and Value of NSCALE

## Slide 3: Challenges and Motivation
PLMN operators provide two different services to Verticals under two different business scenarios:
  Communications services: Operator provide network transmission services, the slice management is as the internal.
  Slice as the services: Operator provide slice service, the slice management is exposed to vertical.
Some large-scale vertical customer would like to purchasing slice services and manage their slices by themselves. To Enable that, they should
  Determine what kind of slice is appropriate for their services before order the service(Slice SLA determination)—GAP: How
  Make an service order -- GAP： by what
  Adjust the SLA according to the real performance of vertical applications—GAP: How
Slice enabler support those functions and provide SDK/API(s) for slice management application developers to build up Application over them.

## Slide 4: Role of NSCE
The NSCE provides the required functions for vertical management application.
  Deployed and located in vertical Domain
  Retrieve application related data（e.g KQI/QoE ) without privacy issue
  Retrieve network/slice information by invoking capabilities and information exposed by operator domain

## Slide 5: Functions for management of slice lifecycle
Example of how vertical customer can be able to manage slice
Step1: Slice preparation
Step2: Slice service subscription
Step3: Slice monitor
Step 4: Slice adaption
SLA determination
Slice Subscription
Slice SLA monitor
Fault monitor
Slice adaption suggestion
Supporting functions by NSCE
Description: Vertical applications requirement => suggested SLA
Implementation example: NSCE platform can compute based on some data from trial, and search the available items (NSaaS Product catalog)
from operators BSS/CSMF
Description: make a slice subscription with the SLA derived from step1:
Implementation example:
invoke API exposed by operator (e.g., CSMF/BSS/NEF)
Description: calculate slice SLA satisfaction
Implementation example:
Computing based on
invoke slice performance information API exposed by operator (NSMF、NEF）
Collected application layer performance information from either client or APP server
Description: Fault alert and diagnose
Implementation example:
Computing based on
Invoke slice fault report APIs exposed by operator(e.g., NSMF)
Collected application layer fault information from either client or APP server
Slice status monitor
Description: calculate the slice vertical info about the logical link between UE and network slices and slice status
Implementation example:
Computing based on
invoke slice information API exposed by operator (NSMF/CSMF/NEF）
Collected the application information from both Server/client side
Description: Slice scaling or policy adjust
Implementation example:
Computing based on
Invoke slice modification APIs exposed by operator(e.g., NSMF)
Invoke the policy control functions exposed by operator (e.g., NEF)
Slice SLA subscription modification
Description: update the SLA subscription information
Implementation example:
Computing based on
Invoke SLA subscription APIs exposed by operator(e.g., CSMF)

## Slide 6: Summary: Value of NSCALE
Production networks are critically important, enterprise services place high requirements on such networks.
How can we ensure the quality of production networks, keep track of Service Level Agreement (SLA), and monitor campus networks in order to prevent and locate fault?
Support diversity services with 5G network
Lack of experience to set requirements on carrier’s 5G network
Manual operations to monitor the campus network
Manual operations to ensure the quality of production networks
Data privacy
APIs from different systems （OSS, BSS, CN）
Challenges
With NSCALE
Network slice management to support diversity services
Assistance on automated requirements translation from verticals perspective to carrier’s 5G network
APIs to expose the performance of the campus network
Automated adjustment to ensure the quality of production networks
Keep the production private data within the campus
Unified APIs to satisfy the verticals requirements