## Slide 1: MSGin5G-SEALDD integration
Catalina Mladin
Source: Convida Wireless

## Slide 2: Outline/ summary
3 approaches for MSGin5G-SEALDD Integration are introduced
The proposed way forward is supported by companion text
Following discussions, the agreed way forward can be reflected in the TR

## Slide 3: Approach 1
Independent services and SID/WIDs; Selected Rel-17 TS 23.554 content reuse for SEALDD
  How: TS 23.554 content may be reused, but feature adoption discussed case-by-case
  Assumption: MSGin5G and SEALDD deployments/services will have little overlap.
  Assumption: MSGin5G will progress independently in Rel-18+
Results:
  Services to be maintained separately
  Duplication of existing work avoided, for the future not envisioned
  Rel-18 SEALDD discussions will be focused heavily on MSGin5G integration
  If deployments overlap, choice of service to use can become issue for providers, interworking can become issue for SA6

## Slide 4: Approach 2
Merged services and SID/WIDs; Rel-17 TS 23.554 advanced by SEALDD
  How: SEALDD SID/WID adopts MSGin5G service, advances TS 23.554, adds features. (“TS merge”)
  How: goal of supporting IoT (i.e. MSGin5G usecases) is clearly and purposely merged into SEALDD 18+ (SID/SID merge)
  Assumption: MSGin5G Rel-17 features are needed in SEALDD, but deployments are best served by a single delivery service.
  Assumption: backward compatibility from R-18 to R-17 is not required. Service renaming TBD.
Results:
  Single service avoids duplication of existing and future work, maintenance.
  Rel-18 SEALDD work boosted by MSGin5G integration, minimal change discussions
  Deployments will deal with single service

## Slide 5: Approach 3(part 1)
SEALDD as “next-gen MSGin5G”; Rel-17 TS 23.554 content reuse for SEALDD
  How: New SEALDD TS adopts entire TS 23.554 content, generates new service. Changes to adopted TS 23.554 content will ensue, changes adoption discussed on a case-by-case basis. Minimization of functional changes is targeted, but gaps are closed and features added.
  How: Evaluate maintaining support for lightweight clients as a KI. Possible solutions include support for two SEALDD client types: “lightweight” vs. “regular”, or distinguishing them by capabilities.
  How: Rel-17 MSGin5G/ TS 23.554 will be supported with CAT-F CRs. Single release service.
  How: goal of supporting IoT (i.e. MSGin5G usecases) is clearly and purposely merged into SEALDD (SID/WID merge)

## Slide 6: Approach 3 (part 2)
SEALDD as “next-gen MSGin5G”; Rel-17 TS 23.554 content reuse for SEALDD
  Assumption: MSGin5G Rel-17 features are needed in SEALDD, but deployments are best served by a single delivery service in the long run.
  Assumption: deployments with Rel-17 MSGin5G can move to SEALDD for Rel-18, w/o backwards compatibility.
Results:
  Single service R-18+ avoids duplication of existing and future work, maintenance.
  Rel-18 SEALDD work boosted by MSGin5G integration, some change discussions
  Deployments with Rel-17 MSGin5G are supported. Rel-18+ service fully supports Rel-17 features, although without backward compatibility to Rel-17

## Slide 7: Summary
Approach 3 is proposed as basis of the solution for MSGin5G-SEALDD Integration
  Next steps if agreed:
    Start capturing in TR 23.700-34 Key Issues and solutions relative to TS 23.554. Include possible issue on maintaining support for lightweight clients.
    Generate draft SEALDD WID for discussion, with scope based on FS_SEALDD and MSGin5G new features.
    Start planning TS 23.554 merge into new SEAL TS (e.g. clause restructuring if needed)