## Slide 1: Discussion on Clarifications regarding SEALDD architecture
Yaxin Wang
Source: Huawei, Hisilicon

## Slide 2: Outline
A general architecture for SEALDD is introduced
Architecture assumption for integrating MSGin5G is clarified
Architecture assumption to support Cache service is introduced

## Slide 3: General Architecture
Role of SEALDD played for APP server
APP server mainly includes 4 parts: communication part, data storage part, signaling and data distribution part, and application service logic part. Communication part and data storage part are generic for different applications.
Communication part, storage part and signaling and data distribution part can be implemented in SEALDD server. The application server just focuses on the service logic processing and consumes the SEALDD services to transmit/store data.
A “SEALDD service engine” may be used to arrange APIs of the enhanced functions to be used for data delivery.
Functions can be implemented in SEALDD server
An example for SEALDD server internal implementation, not standard work

## Slide 4: Architecture integrating MSGin5G
SEALDD integrating MSGin5G
  SEALDD server integrates the MSGin5G functions and expose a general SEALDD API including MSGin5G service or MSGin5G API to application server.
  Application server can send out MSGin5G messages or data traffic along with MSGin5G requirements, after data processing by SEALDD server, the traffic is sent out in MSGin5G format.
An example for SEALDD server internal implementation, not standard work
(as per 23.554)

## Slide 5: Architecture for Cache service
SEALDD support for Cache service
  SEALDD server provides data storage service and data transmission service for application Cache server.
  Application server processes the cache logic and determines whether and how to update/deliver the cached data in SEALDD server.
Application cache logic function could be an Application Server or Cache Server which is part of SEAL, but such application cache logic will not be part of SEALDD scope .
Functions mapped to SEALDD server
An example for Cache server internal implementation, not standard work

## Slide 6
Thank You!