## Slide 1: 5GFLS – Way Forward
Basavaraj (Basu) Pattan,
Samsung

## Slide 2: Outline
1. SEAL – Response to Comments
  Comment#1: SEAL services are heavy to deploy
  Comment#2: SEAL protocol is complex to implement
  Comment#3: SEAL LM is architecturally not suitable to 5GFLS
  Comment#4: SEAL LM and 5GFLS are different functionality and independent
  Comment#5: Common functions should be specified in 5GFLS
  Comment#6: Investigate SEAL LM and 5GFLS architectures separately
2. Architecture Options analysis
3. New Proposal (collocated and distributed deployment)
4. Summary

## Slide 3: SEAL – Response to comments (1/3)
Comment#1: SEAL services are heavy to deploy
Response#1:
SEAL is a service platform that binds 3GPP network with the Vertical Applications. SEAL is not specifically developed for Mission Critical communications but any vertical service.
A service platform offering common capabilities (e.g. Group management, Configuration management, Location management etc) to a variety of verticals/enablers (e.g. V2XAPP, UASAPP, FFAPP, 5GMARCH etc).
SEAL specified in 3GPP Rel-16, continues to add more common capabilities through further 3GPP releases.
It is upto each Vertical specification to define which SEAL service features are leveraged by that Vertical.
Also each SEAL Service Provider can decide what SEAL services to offer towards Verticals. If any feature not offered by the SEAL Service Provider and if required by the Vertical, then such feature has to be implemented at the Vertical Application Layer.
Conclusion: Although there are many SEAL services defined in 3GPP specification, usage of all SEAL services is not mandatory. Each SEAL Service Provider decides what to deploy and leveraging SEAL feature is upto Vertical specification.
Comment#2: SEAL protocol is complex to implement
Response#2:
SEAL service platform caters to multiple Vertical Applications serving wide horizon of devices (e.g. complex smart devices to constrained devices).
SEAL services specifies SIP protocol for heavy devices and also specifies CoAP protocol for constrained devices in Rel-17.
Adding more protocol support in SEAL is natural since it is a service platform and not a service itself.
Each Vertical specification decides which protocol to be leveraged by that Vertical.
If any new protocol needs to be supported in Rel-18, it is possible to do that.
Conclusion: SEAL specifies suite of protocols that supports both complex and light weight devices.

## Slide 4: SEAL – Response to comments (2/3)
Comment#3: SEAL LM specifies location information sharing to non-target UEs which is not applicable in 5GFLS. Hence SEAL LM is architecturally not suitable to 5GFLS.
Response#3:
SEAL LM specifies location information sharing to both VAL Servers and non-target VAL users.
5GFLS requirement is location information sharing to VAL Servers only.
It is in Vertical realm to decide whether to implement and allow location information sharing to non-target VAL users or not. And SEAL allows that flexibility to Vertical Applications.
Conclusion: SEAL is flexible and 5GFLS can ignore the functionality where location information is shared to non-target VAL users.
Comment#4: SEAL LM and 5GFLS are different functionality and independent
Response#4:
1. SEAL LM provides location reporting to the VAL Server or to non-target UE, of the location information acquired e.g. from CN or from UEs via LMC.
2. 5GFLS is mainly about fusing location information from multiple sources to generate accurate location information. Once fused location information is available, it needs to be reported to VAL Server.
Fusing of location information from multiple sources can be responsibility of 5GFLS and SEAL LM can be used for fused location reporting.
5GFLS should not specify location reporting which is already available as SEAL LM service.
Conclusion: SEAL LM and 5GFLS can be complementary but cannot be independent, unless there is duplication.

## Slide 5: SEAL – Response to comments (3/3)
Comment#5: Common functions should be specified in 5GFLS.
Response#5:
SEAL services are themselves common capabilities.
Specifying common functions in 5GFLS means further duplication between SEAL LM and 5GFLS.
Conclusion: Common functions should remain the scope of SEAL LM and not duplicate them in 5GFLS. 5GFLS can also considered for common functions on a case-by-case where there is no duplication with SEAL.
Comment#6: Investigate SEAL LM and 5GFLS architectures separately
Response#6:
In TR 23.700-96 v0.4.0, Solution #1 is capturing Standalone functional architecture for fused location service.
In TR 23.700-96 v0.4.0, Solution #3 is capturing fused location service leveraging SEAL location management.
Technically, both are feasible solutions and should be captured in the study. However, for progressing to normative work, solution evaluation and conclusions should ensure no duplication of work.
Conclusion: Fine with investigating multiple architectures for study. Progressing to Normative work by ensuring no duplication of solution.

## Slide 6: Architecture: Option #1
Fused location – function v/s server
  5GFLS is supposed to be light weight in protocol, implementation and deployment
  Current architecture (Solution#1) showing as Function is correct
Current architecture (Solution#1) has following EN to be resolved
  Editor's Note: It is FFS to show the relationship of Fused Location Function with SEAL-LM.
Proposal in S6-220425 states “As required by the verticals, the Fused Location Server also provides common service capabilities to support location-based applications, i.e. common services to be reused frequently to support e.g. geofencing, location analytics, heatmap etc. The Fused Location Server does not process service requests of a external user (by a non-target UE) directly, i.e. does not process the external user’s request of location-based service,” Common service capabilities is already the core aim of SEAL LM and this concept should be considered while resolving above EN (stated in bullet #3).
Proposal in S6-220425 states FLS-1: “Service-based interface supporting location reporting, location determination, location management and exchange of location contextual information over application layer transactions between the Fused Location Server and the Fused Location Client of the target UE.” Location management including reporting is already specified in SEAL LM. Gaps should be mentioned considering what is currently available.
Solution#1: Standalone functional architecture for fused location service
Option#1: Proposed in S6-220425

## Slide 7: Architecture: Option #2
SEAL LM is responsible for location management functionality including reporting which could be obtained from a source
Showing SEAL LM as one of the producer of location information is not a valid option
From S6-220114_rev1
Figure 4. SEAL LM as location source for Fused Location Server
Proposed in S6-220114_rev1
Last Figure SEAL LM relays location request to Fused Location Server
SEAL LM is responsible for location management functionality including reporting which could be obtained from a source
Showing SEAL LM obtaining location information from fused location function seems fine

## Slide 8: Architecture: New Proposal (1/2)
SEAL LM today obtains location information from either CN or UE
5GFLS proposed to obtain location information from more sources (GMLC, SLP, 3rd party location server) and fuse
Our new proposal is:
Based on Proposal in S6-220114_rev1 Last Figure - SEAL LM relays location request to Fused Location Server
Fused Location Function still keeps the functionality of fusing location information from multiple sources
SEAL LM retains the management aspects including location reporting
Any additional Common service capabilities (geofencing, location analytics, heatmap) could be considered as enhancements to SEAL LM
Flexible deployment options can be captured – Fused Location Function can be collocated or outside (see next slide).
Solution#3: Functional architecture of fused location service leveraging SEAL location management
New proposal – collocated deployment

## Slide 9: Architecture: New Proposal (2/2)
Our new proposal in alternate deployment option:
Based on Proposal in S6-220114_rev1 Last Figure where SEAL LM relays location request to Fused Location Server
Fused Location Function still keeps the functionality of fusing location information from multiple sources
SEAL LM retains the management aspects including location reporting
Any additional Common service capabilities (geofencing, location analytics, heatmap) could be considered as enhancements to SEAL LM or 5GFLS on a case-by-case avoiding duplication with SEAL
Fused Location Function resides outside SEAL LMS.
New proposal – distributed deployment

## Slide 10: Summary
Architecture in Solution #1 and Solution #3 both need to show 5GFLS relationship with SEAL LM considering following principles:
  SEAL LM provides location management that includes location reporting to the VAL Server or to non-target UE, of the location information acquired e.g. from CN or from UEs via LMC.
  5GFLS is mainly about fusing location information from multiple sources to generate accurate location information. Once fused location information is available, it needs to be reported to VAL Server leveraging SEAL LM.
  Role of 5GFLS in Common service capabilities (geofencing, location analytics, heatmap) to be decided case-by-case.
Alternate architectures can be studied but our preferred architecture for normative is as shown on Sldie#8 “New proposal – collocated deployment”. However, alternate deployment architectures (e.g. on Slide#9) can also be captured in normative specification.