## Slide 1: Floor control signalling over QCI 65
Nathan Jeyaratnarajah and S.(Ram) Ramanan
UK Home Office

## Slide 2: Outline
Floor control signalling in 3GPP specs
Issues observed
Summary and next steps

## Slide 3: Floor control signalling in 3GPP specs
TS 23.379 Clause 7.3.1 mentions
  “MCPTT-4 carries unicast floor control signalling between the floor control server of the MCPTT server and the floor participant of the MCPTT UE.”
TS 23.379 Clause 5.7.3 defines
  “ The dedicated bearer for voice and MCPTT-4 reference point messaging shall utilise the QCI value of 65 (as specified in 3GPP TS 23.203 [4]). “
TS 23.203 Table 6.1.7: Standardized QCI characteristics

## Slide 4: Issues observed in our implementation
eNodeB releases QCI 65 e-RAB before RTCP over Disconnect is sent to UE in pre-established sessions
  QCI 65 bearer is released in LTE but MCPTT floor is not released at MCPTT client
    MCPTT client does not return to the call idle state immediately after the ongoing MCPTT call is released from the network
    Sticky floor (floor not released) following a broadcast call
Challenge to meet MCPTT access time (KPI1) requirement for emergency calls due to on-demand establishment of QCI 65 bearer
    The requirement for MCPTT Emergency (Group) Calls: the MCPTT Service shall provide an MCPTT Access time (KPI 1) less than 300 ms for 99% of all MCPTT Requests
Noticeable loss of floor control signalling over RTCP packets

## Slide 5: Release of QCI 65 before Disconnect in our implementation
Call connect and disconnect information flows are sent over non-SIP media plane signalling using MCPTT-4 for including or releasing an MCPTT client in the call using a pre-established session.
In pre-established sessions, we observed that MCPTT calls are ended by MCPTT server by sending “disconnect” message using RTCP message to MCPTT clients
Thereafter, MCPTT server does the bearer release procedure via Rx interface
Sometimes, RTCP packets containing “disconnect” message arrive at eNodeB user plane PDCP layer, after eNodeB has released QCI 65 e-RAB and subsequently “disconnect” message is not delivered to MCPTT clients
As a result, the MCPTT call is not released until a timeout happens.
This impacts MCPTT client’s readiness for new calls.

## Slide 6: Increase in MCPTT access time in our implementation
In pre-established sessions, an MCPTT call is established after an MCPTT client received RTCP: “Connect” message over QCI 65
“Connect” message is delivered to the client after QCI 65 bearer has been established.
There is a time lapse for on-demand establishment of QCI 65 bearer
The time lapse can sometimes be larger than intended
This increases the emergency call set up time beyond the MCPTT access time KPI of 300ms

## Slide 7: Robustness of QCI 65 for media plane signalling
Packet error loss rate of QCI 65 is too high (10-2) for floor control signalling
A reliable signalling requires packet error loss rate at 10-6
QCI 65 is an unacknowledged mode bearer
The floor control signalling messages on QCI 65 can be lost in the air interface due to higher packet error tolerance.
It has been observed that during call setup procedure, “Connect” message using RTCP was not received by MCPTT clients in the lab tests.
The retransmissions can mitigate the loss but may add additional delays
Duplication of floor control packets may alleviate problem at a cost of additional bandwidth
Use of bearer with better PELR may also resolve the problem. This needs changes in the MCS specs.

## Slide 8: Summary
In summary, there are a few observed issues with floor control signalling using RTCP over QCI 65
We would like to explore options to address these issues
Happy to discuss further and bring CRs, if necessary