## Slide 1: Clarification on bundling of EAS(s)
Yajie Hu
Source: Huawei, Hisilicon

## Slide 2: Problem Introduction
Some companies think that there should be no limitation added for bundled EAS(s) to be offered from the same EDN. Bundled EAS(s) should be support across EDNs.
While some other companies think that bundled EAS(s) should be within the same EDN due to the consideration of edge network KPIs and also practical deployment use cases.

## Slide 3: Different types of bundled EAS(s)
AC managed bundled EASs (KI#18: Linkage between EASs)
  The bundle EAS is only within an EDN for ensuring similar network latency to the AC.
  AC connects to each EAS independently
EAS managed bundled EASs (KI#20: Method of supporting federated EAS service)
  AC only need to connects to the main EAS
  The main EAS connects to other EASs in the bundle EAS.
AC
EAS#1
EAS#2
EAS#3
EDN
AC
EAS#1
EAS#2
Main
EAS#3
EDN
1
2

## Slide 4: Summary
We should agree to the following assumption considering the different types of bundled EAS(s)
  Bundled EAS(s) should be within the same EDN due to the consideration of
    edge network KPIs
    practical deployment use cases (ASP deploys the bundled applications in the same EDN of the ECSP).
    Bundled EAS(s) can be registered on to multiple EES(s) in the same EDN of the ECSP.

## Slide 5
Thank You!