## Slide 1: 5G enabled Location based Service
Chunshan Xiong, chunshan.xiong@cictmobile.com
CATT

## Slide 2: Outline
1. 5GFLS Logical Architecture
2. Architecture Options analysis
3. New SID Proposal
4. Summary

## Slide 3: 5GFLS Standalone Logical Architecture
Fused Location Server architecture should include two layers functions:
the first layer function is the Fused Location Function(produces the precise location information) and
the second layer funcgitons is the Core Service Functions.
The FLS can get location information via the 3GPP access as defined in TS29.527 and also can get location information via the non-3GPP defined access
For the non-3GPP defined accesses, the FLS-1 functions:
Get the UE location information;
Provide location notification to the target UE and get guarantee to get location information from the target UE;
Install location event triggers in the target UE to support the target UE terminated deferred location information;
Get the location privacy indication updated by the target UE;
Provide the location assistant data and ciphering key to the target UE;
The Fused Location Server can get different location sources (e.g. SEAL LMs) from multiple PLMNs.

## Slide 4: Merged 5GFLS Architecture Options
SEAL LM just one source of location information for a 3GPP access;
SEAL LM provides location information for all 3GPP accesses;
SEAL LM relays location request to Fused Location Server

## Slide 5: Fused Location Function and SEAL LM
The logical function of FLF (Fused Location Function) focuses on the location information retrieving and can be merged with the SEAL LM.
The FLS can focus on the core location service

## Slide 6: New SID :5G-enabled Location Based Service
1) Based on SA1 service requirements, SA2 positioning service exposure and existing SA6 work, specify architectural requirements, architectural enhancements or new architecture in application layer through the study of following location services:
  Geofencing
  (Indoor) Map provision
  Location Alerting
  Real time Tracing request or playback (continuous locations in a map)
  History Trace request or playback
  Time information of the first entering and the last leaveing an area (e.g. working campus)
  The length of time to stay in an area
  The times to re-enter and re-leave an area
  Location information analysis
  Heatmap
  Speed
  Heading Direction
2) Identify key issues and develop solutions based on aspects above.

## Slide 7: Summary
R18 FS_5GFLS focuses on the location information retrieving and can be merged with the SEAL LM.
New SI FS_5GLCS focuses on how to use the location information and to define the location based services.
The Time and Release information for the new SI FS_5GLCS ?
  Release-19 or Release-18 ?