## Slide 1: Discussion paper on notification management service
Arunprasath R
Source: Samsung, AT&T

## Slide 2: Outline
Description about notification service (PULL and PUSH)
Procedure for receiving notification messages via notification channel
Procedure for re-using the notification channel between NMC and NMS
Architecture requirements, Benefits and Motivation for SEAL Notification management service
NOTE : Some of the slide contents in this discussion document are borrowed from S6-200647.

## Slide 3: Common Notification Service
Notification service requested by the App
Response includes a Callback URL to be used by the App in its request to subscription-to-notification with the App Server
Subscription-to-notifications request contains the “Callback URL” (received in step #2)
Application server sends notifications to the Callback URL (as obtained in step #3)
Notification server delivers the notification received on a Callback URL to the associated application on the UE
Notification Delivery Mechanisms :
PULL
  Based on HTTP request, often referred as “long polling” [RFC 6202]
PUSH
  Websockets [RFC 6455]
  OMA PUSH Enabler
  Device native notification services (such as Android, iOS etc.)
Notifications are conveyed over a “notification” channel
The notification channel has to be created before the delivery
With PULL mechanism, the application clients “polls” notification channel
With PUSH mechanism, the PUSH Enabling is used to deliver the notification to the application client

## Slide 4: PULL Method Notification Delivery
Notification service requested by the App
Response includes a “Poll-channel URL” and a “Callback URL”
Subscription-to-notifications request contains the “Callback URL” (received in step #2)
App initiates a long polling request using the “Poll-channel URL” (received in step #2)
App server sends notifications to the Callback URL (as obtained in step #3)
Notification server responds to the long-polling request which contains the notifications from the App server it received at a specific callback URL

## Slide 5: PUSH Method Notification Delivery
Notification service requested by the App
Response includes a Callback URL to be used by the App in its request to subscription-to-notification with the App Server
Subscription-to-notifications request contains the “Callback URL” (received in step #2)
Application server sends notifications to the Callback URL (as obtained in step #3)
Notification server delivers the notification received on a Callback URL to the associated application on the UE using a PUSH enabling mechanism (e.g. device native notification service) which is identified as part of step #1
Application Server
Notification Server
Application/service
1
2
3
4
5
PUSH Enabler Server
5

## Slide 6: Notification channel creation

## Slide 7: Re-using notification channel
When there is a notification channel already existing between NMC and NMS, NMC may decide to reuse it and just requests for a callback URL from NMS
NMC requests the NMS to reuse notification channel by sending the re-use notification channel request
NMS returns callback URL in the response which needs to be used by the requesting client when subscribing with the server for receiving notifications
NMS if it decides to reuse the same callback URL for different VAL services it can return the same callback URL to NMC

## Slide 8: Architectural requirements to be added
[AR-4.3.9-a] The SEAL shall enable delivery of notification data from vertical applications servers to the vertical applications clients.
[AR-4.3.9-b] The SEAL shall support different delivery mechanisms for notification data (PUSH/PULL), as required by the vertical application.

## Slide 9: Benefits
Common notification delivery service to all vertical applications
Enables delivery of asynchronous notifications to the UE
Simplifies the application notification design
  leave the complexity of actual delivery of notifications from application endpoints to a common notification management service
  Each vertical application client do not have to implement the logic of listening to the service specific callback URL for the incoming notification messages
Flexible notification design for verticals. Even the existing SEAL services can make use of the notification management service for receiving notifications
Consistent way to deliver notifications for all verticals
Cost effective

## Slide 10: Motivation
Propagation of EEL notifications to EEC using Edge Notification Server
Many of the existing VAL services and SEAL services require notification mechanism. And those procedures can be augmented with SEAL notification management service mechanism to deliver the notifications. SEAL notification management service can be added as another alternative. Some of the examples are as below :
  E.g., Message delivery to target geographical areas from the VAE server
  Notifications for network monitoring information
  Pushing ProSe Layer-2 Group ID corresponding to the dynamic group information to the VAE client
  Identity list notification, Group creation notification, group deletion notification etc.,
Upcoming VAL/SEAL services can adapt the SEAL notification management service for supporting notification functionality where applicable
Already supported by MCData service

## Slide 11
Thank You!