## Slide 1: Location Interworking with LMR systems
Mike Dolan
FirstNet

## Slide 2: Outline
Issue
Architectural Solution
Proposal

## Slide 3: Issue
Interworking between LMR and MC systems already supports groups.
When in a 3GPP MC system, authorized clients can obtain the location of other group members.
MC clients can see the location of other group members on the MC system but cannot see the location of other group members on an LMR system, except when that person is talking. This is a gap in LMR-3GPP interworking from Rel-16 onward.
ISSUE: How to make general location information bi-directionally available between LMR systems and MC systems?

## Slide 4: Architectural Solution
3GPP MC systems already can provide a LoCation Services (LCS) server (3GPP TS 23.271 – Release 16).
If the LMR system supports a location function, use the existing 3GPP LCS client to LCS server interface to provide two-way access to location information between the LMR location function and the 3GPP location server.
Apply this solution from Release 16 onwards to support the gap in location interworking between LMR and 3GPP MC systems. And MCPTT user can already know the location of the LMR talker – this solution provides the ability to get the location of all LMR users in a group if the requestor is authorized to have it.
No changes to interfaces or procedures are required in 3GPP Rel-16 and later specs.

## Slide 5: Architecture
LMR Location Function
3GPP Location Server
LMR location clients
3GPP location clients
3GPP LCS client-server interface
per 3GPP TS 23.271

## Slide 6: Proposal
Modify 3GPP TS 23.283 to add text that specifies the use of the LCS client-server interface of 3GPP TS 23.271 to exchange location information between LMR systems and MC systems.
  Keep existing 3GPP TS 23.283 text that indicates the inclusion of the location of the talker in the user plane.
Apply this fix to close the gap in location information availability from Rel-16 onward.