## Slide 1: ETSI MEC reply to the LS (S6-221436) from 3GPP SA6 (attachment to the LS reply)
27/07/2022
At：MEC Tech#253
1
From：ETSI ISG MEC
MEC(22)000269r3
For Discussion &Decision

## Slide 2: Topics for alignment with EDGEAPP
As per the LS received by SA6, ETSI MEC agrees that the alignment aspects in the present release of this specification includes the following:
  alignment of EAS profile (EDGEAPP) and appInfo (ETSI MEC),
  alignment of EDGE-3/Mp1 reference points
  alignment of EDGE-9/Mp3 reference points
  usage of CAPIF between the two architectures
Also, in the LS it is stated correctly that the term alignment does not imply that the reference points will be exactly equivalent.
The following slides provide a preliminary assessment on the current level of alignment, for each of the above 4 topics suggested by SA6.
  Note for the reader: we present first of all topic#2 for better understanding on the other items

## Slide 3: 2. alignment of EDGE-3/Mp1 reference points
Status (ETSI GS MEC 011)
  The Mp1 reference point between the MEC platform and MEC application instances provides two API groups:
    MEC service management API: service registration, service discovery & communication support for services. An informative Annex on “Mapping MEC service management API to CAPIF APIs” is provided.
    MEC application support API: application availability, session state relocation support procedures, traffic rules and DNS rules activation, access to persistent storage and time of day information.
  Registration is identified as a common functionality
    Baseline MEC application instance registration procedures (over Mp1) are captured (register/deregister/update/query) is MEC 011 v3.0.6, with associated stage 3 API definitions.
    Registration enables an MEC application instance to provide its information and is available to all applications, regardless of whether they are orchestrated by the MEC system management or not.
    For applications not orchestrated by the MEC system management, registration can ensure the application instance is discoverable and enables it to utilize the services provided by the MEC system.
Assessment
  The basic alignment objective is to provide a unified API (at least the same functionalities) to app developers.
  Coordination with 3GPP SA6 (stage-2) and CT3 (stage-3) to achieve closer alignment.

## Slide 4: 1. alignment of EAS profile (EDGEAPP) and appInfo (ETSI MEC)
Status
  In the current version of GS MEC011, a baseline MEC application registration with a baseline data type AppInfo is captured with editor’s notes for further updates.
Assessment
  The basic principle of the alignment is to provide a unified API (at least the same functionalities) to the app developers.
  The idea of the app registration is to also allow the app instances that are not lifecycle managed by the MEC system to be able to utilize the services provided by the MEC system.
  More work for better alignment is needed, which requires close coordination with 3GPP SA6 (stage-2) and CT3 (stage-3).
Note: A kind reminder that the GS MEC 011 deliverable is available at the MEC Open Area: https://docbox.etsi.org/ISG/MEC/Open

## Slide 5: 3. alignment of EDGE-9/Mp3 reference points
Current Status:
  The EDGE-9 reference point enables interaction between two EESs (ref. 23.558).
  The Mp3 reference point between MEC platforms (ref. GS MEC 003) is used for control communication between MEC platforms. Optionally, control signaling can be exchanged between two MEC platforms in different MEC systems in order to facilitate feature specific inter-MEC system coordination.
Assessment and additional considerations:
  Both reference points are quite aligned, although not much specified.
  In addition, no major updates on Mp3 is foreseen (e.g. for OP compliance purposes, where Mff is considered for EWBI).

## Slide 6: 4. usage of CAPIF between the two architectures
Current Status:
  MEC and CAPIF both provide service registries. Stage 2 is well aligned.
  The ISG identified some differences in the stage 3:
    Different sets of filter parameters for querying the registries
    CAPIF only supports REST, MEC supports REST and additional "alternative transports"
    MEC supports heartbeat, CAPIF does not (TBC)
    Even though both are based on OAuth 2.0, security mechanisms slightly differ
  Assessment and considerations:
  Further communication and coordination with the relevant 3GPP WGs (SA6 for stage-2, CT3 for stage-3 and SA3 for security related issues) are required to achieve better alignment on CAPIF.

## Slide 7: Conclusions
ETSI MEC agrees on the need for alignment between ETSI MEC and 3GPP SA6, especially on the 4 topics suggested by SA6
The present slides provided a preliminary assessment on the current level of alignment, for each of the 4 topics.
ETSI MEC plans to work on these aspects and is willing to continue the alignment with SA6.

## Slide 8
Follow us on:
Thank you for your attention