## Slide 1: Way forward for federation and roaming
Nishant Gupta
Delegate, Qualcomm

## Slide 2: Outline
Overview
Flowchart
Step 6
Different approaches in detail
Proposed way forward

## Slide 3: Overview
Rel-18 eEDGEAPP aims to specify:
Federation of ECSPs, to share resources and allow subscribers of partner ECSPs access to these resources.
  Suggestions have been made to name this feature ‘Inter-ECSP service roaming’
EEL support for UEs roaming to a different PLMN
While availing services of the federation, UEs may or may not be roaming to a different PLMN.
Different views have been expressed on navigating an EEC or a S-EES for service provisioning in the above scenarios.
In all different options, either “ECS configuration information” or “EDN configuration information” to connect to an available EES needs to be provided to the EEC/S-EES.

## Slide 4: Flowchart
  *In step 3, contacted ECS may not have a suitable EDN available due to multiple reasons, such as, not having the required application deployed, not serving via UE’s current serving-PLMN in case the UE is roaming, etc.

## Slide 5: Step 6
The contacted ECS needs to determine a partner ECS that can provide the application required by the EEC/EES, as indicated in step 1a/1b.
Considering different business models, multiple options have been discussed to enable step 6:
  Pre-configuring the ECS with relevant information
  OAM based ECS configuration
  A searchable repository

## Slide 6: Different approaches in detail
Pre-configuring the ECS with relevant information
  Being relatively static, ECS configuration Information can be pre-configured. EES and EAS (deployment) information cannot be pre-configured.
  ECS configuration may include attributes (such as PLMN IDs, partner ECSP IDs etc.) to select an appropriate ECS that can serve the EEC.
  Availability of the required application via the ECS(s) can not be verified; unless the contacted ECS queries the candidate ECS(s) individually.
OAM based ECS configuration
  Enhance roaming agreements (and other relevant OAM configurations) with application availability information.
  Ensure that service agreements with the end user and the federation agreements between the ECSPs cover application details.
  Enhance the agreements as and when required to add newly (un)available applications.
  Application availability can be ensured; however, such restrictive agreements do not suit all business models.
A searchable repository
  Create a repository of available ECSs and associated application IDs
  ECSs query this repository to find a partner ECS that has the required application available
  Application availability is verified, and the model fits most business requirements; however, it requires maintaining the repository and real-time check as needed.

## Slide 7: Proposed way forward
All 3 approaches are valid for different business models and assumptions.
Incorporate all 3 approaches in step 6.
Step 5: ECS determines that information of a federation partner needs to be provided.
Step 6a: ECS checks availability of any preconfigured or OEM configured information.
Step 6b: If required information is available, ECS proceeds with step 7.
Step 6c: If not, ECS queries the repository and seeks relevant ECS information.
Step 6d: If available, ECS proceeds with step 7; otherwise ECS sends a negative response back to the requestor.
Step 7: ECS checks if EEC/EES can directly contact the partner ECS.
See related pCR in S6-222303.

## Slide 8
Annex

## Slide 10: Enhanced ECS
Edge Configuration Server (Edge Repository)
ECS that acts as edge repository (ECS-ER) provides supporting functions needed for roaming and federation. Functionalities of ECS-ER are:
a) Receiving and storing information about edge computing resources from other ECS(s) of the federation;
b) Providing information about Edge computing resources to other ECS(s) of the federation.
EDGE-10
EDGE-10 reference point enables interactions between the ECS and the ECS acting as edge repository. It supports:
a) Registration and de-registration of the ECS to the ECS acting as edge repository; and
B) Retrieval or discovery of information about other ECS(s) of the federation.