## Slide 1: Discussion on VAL Data Collection Management Service
JIA Xiaoqian
Huawei

## Slide 2: VAL Data Collection Mmanagement Function
To achieve the end-to-end application enablement for verticals, the data collection from end users are needed.
  The procedures of data collection from the VAL client and VAL server are captured across different studies, e.g., NSCE, ADAE, SEALDD…
  To provide a unified interface of VAL data collection, a VAL Data Collection Management function is needed.
  As the figure shows, the VAL Data Collection function is responsible for the data collection provisioning and data reporting configuration. The interfaces of DCM-UU and DCM-S are involved.
Notes: 需要有一个统一的data collection function

## Slide 3: Coordination Between DCM service and other SEAL services
  VAL Data Collection Management function provides the data collection management services to other SEAL functions which require to collect data from VAL client, or VAL server, e.g., NSCE, ADAE, SEALDD…
SEAL generic functional model representation using service-based interfaces illustrates the coordination between DCM service and other SEAL services.

## Slide 4: Data Collection AF(DCAF) in SA4
  Reference architecture for data collection and reporting is defined in SA4, TS 26.531 for purpose of application Data Collection requested by NWDAF.
  - The Data Collection AF is responsible for UE Application(s) data collection and reporting.
  The Data Collection AF is registered with the NRF and updates the set of available NF profile(s) in the NRF.
  The Services related with DCAF are exposed to parties outside the trusted domain Via NEF.
  In some scenarios, the verticals data is private and required to be stored, analyzed and managed in the vertical domain, the VAL data collection service based on SEAL architecture only and decoupling with Core Networks are required.

## Slide 5: Data Collection APIs related with DCAF
  - R1 supports the interactions between a Provisioning AF in the Application Service Provider and the Data Collection AF, including data collection and reporting provisioning.
  - R2 supports the interactions between the Direct Data Collection Client in the UE and the Data Collection AF, including data collection and reporting configuration and sending data reports.
  - R4 supports the interactions between the Application Server (AS) and the Data Collection AF, including data collection and reporting configuration and sending data reports.
Followings are relevant interfaces and their corresponding purposes.

## Slide 6: Proposals
Proposal 1: Define VAL Data Management Function based on SEAL architecture.
Proposal 2: Consider the following two options to move forward.
Option i: Define a DCMF (Data Collection Management function) based on SEAL architecture by reutilizing the DCAF and corresponding generic APIs defined in SA4. In this option, a LS to SA4 is needed to ask for the decoupling between DCAF and Core Network Function.
Option ii: Define a DCMF (Data Collection Management function) with no dependencies with DCAF in SA4.
Proposal 3: Further define the details of APIs and information flows in different scenarios and for different applications if needed.