## Slide 1: VAL Service Area
Arunprasath R (arun.prasath@samsung.com)
Samsung

## Slide 2: Outline
VAL service Area
Current use of location information
Using VAL service area ID
Summary

## Slide 3: VAL Service Area
Interpretation of Location means different to different entities depending upon the context. For example, for a consumer, location is invariably civic address. For Network, it is one of Tracking Area/Routing Area (TA/RA), eNODEB ID, Cell ID. For a Vertical Application Layer (VAL), it can refer to the jurisdictional area of service.
Every vertical application server will have an area defined within which it provides the required service to the VAL users.
VAL service area can be defined through geographical co-ordinates and can be assigned an ID (VAL service Area ID)

## Slide 4: Current use of location information
Currently the VAL servers share the geographical area with the SEAL servers for the following :
  Get UE Information request from VAL server to SEAL LM server to get the list of UEs in a particular geographical area
  Location area monitoring subscription request from VAL server to SEAL LM to get the list of UEs as and when they move in or out of a particular location
  Location based group creation request from VAL server to SEAL GM to create a group with the list of UEs in a particular geographical area
In all the above cases the VAL server can share the VAL service Area ID as attribute instead of sharing the geographical co-ordinates.

## Slide 5: Using VAL service area ID
VAL server can register with the SEAL service the list of VAL service areas and the corresponding VAL service area IDs. This can happen only once and whenever there is a change in the VAL service area.
SEAL server maintains the mapping between the VAL service area (Geographical area) and the corresponding VAL service area ID.
Once the mapping/configuration of VAL service area and VAL service area ID is created the VAL server and SEAL servers can talk using the VAL service Area IDs instead of the location co-ordinates.
More than one VAL service area can be registered by the VAL server based on the VAL administration input.

## Slide 6: Using VAL service area ID
Once the VAL service area ID mapping is created, VAL server/SEAL servers can use the VAL service area IDs in the following :
  Location Report and location information notification from SEAL LM to VAL server can carry the VAL service Area ID in addition to location information. SEAL server can add the VAL service area ID corresponding to the location information
  GET UE(s) information request can carry the VAL service area ID instead of the geographical co-ordinates
  Monitor location subscription request can carry the VAL service Area IDs as areas of interest.
  Location area monitoring subscription request can include the VAL service Area ID as location information criteria
  Location based group creation
  Location based group update

## Slide 7: Summary
In summary usage of VAL service Area ID brings in more flexibility when using or consuming the functionality from SEAL involving location information.
VAL service area ID can be shared across the SEAL servers and any change/update in the VAL service area can be easily managed. When there is change / update in VAL service Area, then VAL server can just update the VAL service area at SEAL domain only once and need not update its subscription to various APIs where location information is utilized.
                THANK YOU