## Slide 1: Discussion on UEId retrieval for NATed UE IP address
Shahram Mohajeri (AT&T)

## Slide 2: Contents
Overview of the NATed UE IP Address problem
Rel-18 EDGEAPP Study attempt in solving the problem
Background on existing EES UE Identifier API
Option #1 solution description
Option #1 solution – high level call flow
Option #2 solution description
Option #2 solution – high level call flow
Summary
Way forward

## Slide 3: Overview of the NATed UE IP Address problem
Nnef_UEId_Get opertion in Rel-17 doesn’t support NATed UE IP Address
  TS 23.502 clause 4.15.10:
    NOTE 3: The case where UE IP address provided by the AF to the NEF corresponds to an IP address that has been NATed (Network and Port Address Translation) is not supported in this release.
Recent LS (S6-221953) to SA2 and the LS reply from SA2 (S6-223087) reconfirmed the above
  SA6 Question: “Can SA2 support taking NATed UE IP address as input and then expose the UE External ID to EES?”
  SA2 Answer: as per NOTE 3 in TS 23.502 above“…there is currently no specification support for exposure of UE External ID based on the NATed UE IP address.”
  In stage 3 (TS 29.522) Nnef_UEId_Get maps to the following endpoint
  EES requesting to “retrieve” AF-specific UEId using a NATed UE IP address as input would result in an error response (HTTP “404 Not Found“)

## Slide 4: Rel-18 EDGEAPP Study attempt in solving the problem
In Rel-18 EDGEAPP Study, solution #23 is based on having EES invoke the Nnef_UEID API with UE’s private IP address. However, for large network deployments due to private IP address reuse, solution #23 is not workable.
Related Q/A from the recent LS (S6-221953) to SA2 and the LS reply from SA2 (S6-223087) as shown below is not promising:
  SA6 Question: “In certain deployment when multiple UEs are allocated with the same private IP address, can SA2 support addressing IPv4 address overlap issue?”
  SA2 Answer:
    “when this same private IP address is allocated to different UE(s) for different DNN and S-NSSAI(s) by associating the AF with a DNN and S-NSSAI
    Otherwise and furthermore, the "ipDomain" attribute as defined in TS 29.514 clause 4.2.2.2 Note 3 may be leveraged
    The above DNN/S-NSSAI or ipDomain attribute is not expected to be exposed outside the 5GC network.”

## Slide 5: Background on existing EES UE Identifier API
Rel-17, TS 23.558 has defined Eees_UEIdentifier API with a single operation called “Eees_UEIdentifier_Get” which can be used by EAS to retrieve the AF-specific UEId for a given IP Address (aka User Info.)
This operation is a direct RESTful API call between the EAS and the EES
In stage 3 (TS 29.558) “Eees_UEIdentifier_Get” maps to the following endpoint:
e.g. POST https://example.com/eees-ueidentifier/v1/fetch

## Slide 6: Option #1: solution description
An IPv4 EAS instead of making a direct RESTful API call (i.e. POST ../fetch) to the EES
  Would take advantage of the UE’s dual-stack and
  Redirect the UE (via HTTP 302) to a newly introduced EES endpoint:
    {apiRoot}/eees-ueidentifier/<apiVersion>/redirectedFetch
EES “redirectedFetch” is an IPv6 endpoint registered in DNS
  Causes, the UE to switch to its IPv6 stack (i.e. UE is assigned an IPv6 address by 5GC as it redirects to EES’s “redirectedFetch” endpoint)
Net result: EES sees the UE’s IPv6 address and uses it to invoke Nnef_UEId_Get service which will successfully return the AF-specific UEId
In stage 3 “Eees_UEIdentifier” API would introduce an additional new endpoint (as highlighted):
{apiRoot}/eees-ueidentifier/<apiVersion>
/fetch
/redirectedFetch

## Slide 7: Option #1: solution description (Cont’d)
EES in stage 2 (TS 23.558) would introduce a new service endpoint
  i.e. a new operation in the existing Eees_UEIdentifier API called “Eees_UEIdentifier_RedirectedGet”
This new EES service endpoint is to be used only by IPv4 EASs for redirecting the UE’s (via HTTP 302) to this endpoint in order to retrieve the UEId
  i.e. an IPv4 EAS, in MNO networks where NAT is used, would be informed (at onboarding) to use this new “Eees_UEIdentifier_RedirectedGet” operation (as opposed to “Eees_UEIdentifier_Get” operation) to retrieve the UEId
  At onboarding, EAS also provides a redirect-URI and a notification-URI which will be used by EES to return the UEId either via an in-band redirect (HTTP 302) or an out-of-band notification method
Note: The new API request is an indirect call from EAS to EES through the UE
  While the reply from EES to EAS carrying the UEId can be indirect through the UE or direct via notification
API Name | API Operations | Operation Semantics | Consumer(s)
Eees_UEIdentifier | Get | Request/Response | EAS
 | RedirectedGet | Request/Response | EAS via UE redirect (HTTP 302)
23.558: Table 8.6.5.4.1-1

## Slide 8
App client
on UE
EAS
(IPv4)
1. GET (some application request) SourceIP addr = NATed IPv4
3. HTTP 302 redirect: GET {apiRoot}/eees-ueidentifier/v1/redirectedFetch?Seq=xyz
2. EAS needs UEId (then will redirect the UE to get the UEId by pointing it to the EES’s redirectedFetch endpoint )
EES
{apiRoot}/eees-ueidentifier/v1/redirectedFetch
NEF
5. Nnef_UEId_Get ( UE-IPv6-addr, AFId)
6. Response (AF-specific-UEId=1234567abcd)
7. HTTP 302 redirect: GET EAS1.com?Seq=xyz, AF-specific-UEId=1234567abcd
Alternative “A”: return UEId to EAS via an EAS-registered redirect-URI
Alternative “B”: return UEId to EAS via notification at an EAS-registered notification-URI
4. UE’s source IP address is IPv6 =2001:db8:3333:4444:5555:6666:7777:8888
NOTE: Now EES can invoke a Nnef_UEId_Get service with UE’s IPv6 as input
8’. Notify (Seq=xyx, AF-specific-UEId=1234567abcd)
Option #1: solution/high level call flow
7’. HTTP 302 redirect: GET EAS.com?Seq=xyz, ack-Ok

## Slide 9: Option #2: solution description
EEC reuses the EES’s existing Eees_UEIdentifier API
  Hence, minimal stage 3 work
EEC uses UE’s IPv6 address to invoke the Eees_UEIdentifier API
  This is to get around the private IP address reuse issue which is not addressed by Solution #23 of EDGEAPP Study (23.700-98)
  An EES-deployment matter (i.e. which ensures that when needed (e.g. in order to overcome the private IP address overlap issue), the Eees_UEIdentifier service is designated as an IPv6 endpoint in DNS so that EEC Eees_UEIdentifier API call forces the UE to be assigned an IPv6 by 5GC)
Solution #23 of EDGEAPP Study (23.700-98) is adjusted so that AC’s Edge UE ID request to the EEC doesn’t need to provide the UE’s private IP address
23.558: Table 8.6.5.4.1-1
API Name | API Operations | Operation Semantics | Consumer(s)
Eees_UEIdentifier | Get | Request/Response | EAS, EEC

## Slide 10
Option #2: solution/high level call flow
Note: in step 2, the source IP address of the request contains UE’s IPv6

## Slide 11: Summary
Option #1: EAS to force the UE to obtain an IPv6 Address by redirecting the UE to a new IPv6 endpoint exposed by EES
  It requires EES to expose a new endpoint (used for redirect interaction through the UE by EAS as opposed to direct RESTful API interaction with the EAS)
  Requires stage 3 and SA3 work
Option #2: EEC to invoke the existing EES Eees_UEIdentifier API
  Minimal stage 3 changes
  Mainly an EES deployment matter (registering EES Eees_UEIdentifier as IPv6 endpoint in DNS) & little tweaks to Solution #23 of 23.700-98
Common Characteristics of both options:
  Relies on dual-stack UEs
  Requires additional efforts on the part of the Edge App developers
  Exclusive solution for EDGEAPP (i.e. Still non-EdgeApp AFs have the issue of NATed IP address not supported by Nnef_UEId_Get API)

## Slide 12: Way forward
It is proposed to agree with option #2 solution as it requires less Spec efforts and it is inline with the documented solution #23 of EDGEAPP Study (23.700-98)
  Corresponding contributions (S6-230038 & S6-230039) proposing the required changes to 23.558 are submitted to this meeting
It is proposed to send an LS to SA2 (CC SA3) to get their views on option #1 approach (i.e. HTTP 302 Redirect) as a new NEF service endpoint in support of both Edge-enabled & non-Edge-enabled AFs needing to obtain AF-specific UEId for NATed IP address in dual-stack UEs
  LS draft will be provided for SA6#53 meeting
  Potentially targeting Rel-19