## Slide 1: Background information on CAPIF extensibility requirements
Nokia, Nokia Shanghai Bell, Apple, Intel, Huawei

## Slide 2: Motivation
This contribution provides background information regarding the added requirement and API guidelines updates related to protocol extensibility based on the latest additions to CAPIF, TS 23.222.
These requirements and guideline updates were added to fulfil a request from ETSI ISG MEC who intend to re-use CAPIF, as set out in a LS (S6-222714 / C3-225017).
The additions enable the extension of CAPIF to consider other application protocols for the communication between API invoker and AEF beyond the choice of REST that is currently the only protocol supported by CAPIF.
  NOTE: Such extensions will enable CAPIF to support AEFs with non-REST NBIs defined by other SDOs such as ETSI MEC but won't affect AEFs defined by 3GPP such as SCEF and NEF as per 3GPP's current protocol choice.
A deliberate choice has been made by SA6 to not update the individual information flows in 23.222 w.r.t. extensibility but leave that to CT3 and SA3.
This contribution provides background information related to some items discussed in SA6, to support potential design decisions by CT3 and SA3.

## Slide 3: MEC Requirement 1: Extensible sets of protocols and data formats
"Allow ETSI ISG MEC to extend enumerations, e.g., for data formats, protocols and security mechanisms, without breaking "native" CAPIF API invokers."
CAPIF so far only supports the HTTP protocol. Goal: add more protocols to the published / discoverable service API descriptions.
Same for data formats (only JSON supported) and security mechanisms (which are related to the protocols).
Ensure that extended information will not confuse "native" CAPIF implementations.
 This is covered by the general protocol extensibility requirement [AR-4.11.2-c] in clause 4.11.2 of 23.222.

## Slide 4: MEC Requirement 2: Extension containers
"Support extension containers that would allow an "extended" CAPIF AEF to provide additional information […] during service API publication, persist such extension containers by CAPIF and return them as part of the discover service APIs result."
External SDO defines additional service attributes to describe REST extensions or alternative API architectures e.g. RPC, message bus.
In the API publication request, such additional extension attributes need to be carried ("tagged and bagged") in “extension containers”.
Subsequently, the actual content of "extension containers" is stored by CCF
In the API discovery response, the "extension containers" with their content are provided back to the API invoker.
If extensions are defined by an external entity, these extension attributes would need to use the 3GPP defined "extension container" mechanism. If defined by 3GPP, these extensions can be built directly into the data model.
 This is covered by the requirement [AR-4.2.2-f] in clause 4.2.2 of 23.222.
Potentially affected information flows
Service API information in
8.3.2.1 Service API publish request
8.5.2.2 Service API get response
8.6.2.1 Service API update request
8.7.2.2 Service API discover response
8.25.2.1 Interconnection API publish request
8.25.2.4 Interconnection service API discover response

## Slide 5: MEC Requirement 3: Extensible queries
"Provide a mechanism that allows definition of additional filtering criteria for discover service API queries."
Some of the information attributes in an extension container may also be needed as search criteria during the "Discover service APIs" procedure
This enables specifying "API invoker's interest" (as in Req. [AR-4.2.2-b]) also in terms of information originating from data model extensions.
 This is covered by the requirement [AR-4.2.2-f] in clause 4.2.2 of 23.222.
Potentially affected information flows
Query information in
8.7.2.1 Service API discover request
8.25.2.3 Interconnection service API discover request

## Slide 6: Conclusion
SA6 suggests CT3 and SA3 to take the background information on the previous slides into account.
In particular, SA6 recommends CT3 and SA3 to consider extensibility points in the information flows listed on slides 4 and 5.