## Slide 1: Discussion on CAPIF client agent
Yuji Suzuki
NTT DOCOMO

## Slide 2: CAPIF client agent
In Solution #5 of TR 23.700-95, the CAPIF client agent is approved.
This could be an entity to reduce the number of CAPIF interactions per UE, as it can manage different ACs on the same UE.

## Slide 3: CAPIF architecture
From CAPIF’s point of view, the CAPIF functions can only recognize the API invoker.
ACs behind the API invoker do not appear in the CAPIF functional model.

## Slide 4: Security concern of CAPIF client agent
If a CAPIF agent is authorized to invoke a certain API as an API invoker, that might imply that any applications can trigger the API without the user’s permission to each application.
The authorization function is not able to tell which app is triggering the API invocation.
Therefore the CAPIF client agent needs to perform additional authorization based on application identity.
CAPIF client agent
(API invoker)
AC
(Map app)
AC
(Game app)
UE A
Resource owner
UE B
Authorization funtion
Location API invocation request
Which app is triggering the API invocation?
Use location info

## Slide 5: Proposal
It is optional whether the apps on the UE use the CAPIF client agent or not.
The CAPIF client agent can be seen as one of the individual API invokers on the UE.
No enhancement on the existing specification is required to support CAPIF client agent.
CAPIF client agent
(API invoker)
AC
AC
AC
AC
(API invoker)
AC
(API invoker)
 Not shown in CAPIF architecture
API invocation
UE