## Slide 1: Migration service de-authorization procedure
Kiran Kapale (kiran.kapale@samsung.com)
Samsung

## Slide 2: Outline
Background
Problem Overview
Option #1 solution description and call flow
Option #2 solution description and call flow
Option #3 solution description and call flow
Summary
Conclusions

## Slide 3: Background
TS 23.280 clause 10.6.3 - Migration to partner MC system
  The specification has defined the procedure for service authorization for migration to a partner MC system using migration service authorization request and response.
  The primary and partner MC service server stores the necessary information related to the migrated MC service user (e.g., MC service ID of the migrated MC service user provided by the primary MC system mapped to the MC service ID of the migrated MC service user provided by partner MC systemand the migration status of the MC service user).
  The stored necessary information of the MC service user allows proper communication redirection back to the primary MC system or partner MC system.

## Slide 4: Problem Overview
The MC service allows the MC service user to migrate from primary MC system to partner MC system, migrate from partner MC system to another partner MC system or return back to MC service user’s primary MC system.
Once the MC service user successfully authorized to migrate to a partner MC system by the primary MC system, the partner MC system which is a migrating MC system and primary MC system will store the migration status information along with the MC service IDs from both primary MC system and partner MC system.
This stored information is used in order to route the call appropriately in both primary MC system and partner MC system.
Once the migrated MC service user return back to Primary MC system or migrate to another partner MC system the stored information is to be cleared or updated.

## Slide 5: Problem Overview (Continued)
This stored information is used by primary MC system to route the call appropriately after the migration service authorization and before the user service authorization completes then call routing will be inappropriate and results into call failure.
This stored information is used by partner MC system to route the call appropriately once the MC service user return back to Primary MC system or migrate to another partner MC system then call routing will be inappropriate and results into call failure.
There is no procedure defined in the specification to update or clear the stored information in the partner MC system, which is nothing but Migration service de-authorization procedure.
The MC service authorization is required to receive any MC service from the MC system.
To overcome all the above problems we need an Migration service de-authorization procedure and when to trigger this procedure to avoid the call failures (intermittent service failure)

## Slide 6: Option #1: solution description
The migration service de-authorization procedure initiated by MC service user.
  The MC service user at MC service client is executing all the procedures related to migration service authorization, migration service de-authorization and MC service authorization.
  The MC service user at MC service client triggers the migration service de-authorization procedure when migrated MC service user wants to return to the primary MC system or migrate to another MC system.
  The migration service de-authorization request is sent by migrated MC service user at MC service client on determining that MC service user is no longer migrated to current partner MC system.
  This request is sent only after completing successful MC service authorization at the newly migrated MC system (i.e. Primary MC system to which the MC service user returned back or another partner MC system to which MC service user has migrated).

## Slide 7
Option #1: solution call flow

## Slide 8: Option #2: solution description
The migration service de-authorization procedure initiated by MC service server on completing of migration service authorization.
  The MC service user at MC service client completes the migration service authorization procedure during migration to partner MC system.
  The MC service server of primary MC system triggers the migration service de-authorization procedure towards the previously migrated MC system when migrated MC service user wants to migrate to another MC system.
  The migration service de-authorization request is sent only after completing successful migration service authorization at the newly migrated MC system ( i.e. another partner MC system to which MC service user has migrated).
  The migration service authorization procedure is executed only when MC service user migrating to another partner system but not in case of MC service user returning back to the primary MC system. Due to this, the proposed solution caters only in case of user migrating to partner system.
  The migration service de-authorization procedure is executed before the MC service user completes the MC service authorization at newly migrated system. The call routing will be in appropriate during this.

## Slide 9
Option #2: solution call flow

## Slide 10: Option #3A: solution description
The migration service de-authorization procedure initiated by MC service server on completing of MC service authorization at primary MC system.
  The MC service user at MC service client completes the MC service authorization procedure while returning back to the primary MC system.
  The MC service server of primary MC system triggers the migration service de-authorization procedure towards the previously migrated MC system.
  The migration service de-authorization request is sent only after completing successful MC service authorization at the newly migrated MC system (on return to the primary MC system).

## Slide 11
Option #3A: solution call flow

## Slide 12: Option #3B: solution description
The migration service de-authorization procedure initiated by MC service server on completing of MC service authorization at partner MC system.
  The MC service user at MC service client completes the migration service authorization procedure during migration to another partner MC system.
  The MC service server of primary MC system triggers the migration service de-authorization procedure towards the previously migrated MC system when migrated MC service user wants to migrate to another MC system.
  The migration service de-authorization request sent by primary MC system only after completing successful MC service authorization at the newly migrated MC system and on receiving the notification about the same by the primary MC system ( another partner MC system to which MC service user has migrated).
  The primary MC system should be notified about the successful MC service authorization at the newly migrated MC system.

## Slide 13
Option #3B: solution call flow

## Slide 14: Summary
Option #1: The migration service de-authorization procedure initiated by MC service user
  This solution works for all the cases like user migrating to partner system, returning back to primary MC system from migrated MC system, and migrating to another partner MC system.
  The MC service client is the one who is triggering the migration service authorization and it make sense that MC service client send the migration service de-authorization.
  The execution of migration service de-authorization after successful MC service authorization will ensure the continuation of the service during this process and route the call correctly.
Option #2: The migration service de-authorization procedure initiated by MC service server on completing of migration service authorization.
  This solution works for only in the cases like user migrating to partner system, and migrating to another partner MC system, but doesn’t work.
  The execution of migration service de-authorization after successful migration service authorization will not ensure the continuation of the service during this process and route the call correctly.

## Slide 15: Summary (Continued)
Option #3A and 3B: The migration service de-authorization procedure initiated by MC service server on completing of MC service authorization at primary MC system AND
Option #3B: The migration service de-authorization procedure initiated by MC service server on completing of MC service authorization at partner MC system.
  This solution works for all the cases like user migrating to partner system, returning back to primary MC system from migrated MC system, and migrating to another partner MC system.
  The MC service server at primary MC system is the one who authorized the migration service authorization and it make sense that the MC service server at primary MC system send the migration service de-authorization.
  The execution of migration service de-authorization after successful MC service authorization will ensure the continuation of the service during this process and route the call correctly.

## Slide 16: Conclusions
It is proposed to agree with either option #1 solution or option #3A and #3B solution as :
  It covers all the use cases like user migrating to partner system, returning back to primary MC system from migrated MC system, and migrating to another partner MC system.
  Ensures the call routing during entire migration procedure including the MC service authorization.
  The stored migration information of the user is cleared using migration service de-authorization procedure on condition of successful MC service authorization.

## Slide 17: Thank You!