## Slide 1: Application Service Management
Sapan Shah
Samsung

## Slide 2: Outline
Comparison (Similarities and Differences) between
  Solution #1: Application Service Management Service
    In FS_ACE_IOT
  Solution #5: Service experience to support application performance analytics
    In FS_ADAES
Proposal for normative work

## Slide 3: Comparison – Key Issue being solved
FS_ACE_IOT (Solution #1: Application Service Management Service)
  Provides solution for Key issue #2: Application server monitoring and control of traffic
  Particularly solves following open issues:
    How to enhance the enabler layer (e.g., SEAL, CAPIF) to support service monitoring of third-party application servers?
    How to monitor a third-party server's operational status e.g., congestion levels, failure, and unavailability of the third-party server? How to control/influence the traffic when the third-party application server is experiencing congestion or failure, and when normal operation resumes?
FS_ADAES (Solution #5: Service experience to support application performance analytics)
  Provides solution for Key issue #1: Support for application performance analytics
  Particularly solves following open issues:
    what data needs to be collected from 3GPP system and application specific layer for performing application QoS related analytics?
Observation #1: Both solutions are addressing open issue related to collecting application status/data.

## Slide 4: Comparison – Architecture
Application Service Management Architecture as specified in clause 5.1.1.2 of TR 23.700-97
Application data analytics enablement Architecture as specified in clause 5.3.2 of TR 23.700-36
Observation #2: Both solutions works on almost similar architecture.

## Slide 5: Comparison - Procedures
Observation #3: Push service experience report procedure is defined in both TR 23.700-36 and 23.700-97, where the client pushes similar information to the server.
Information element | Status | Description
VAL UE ID | M | Identity of the VAL UE
VAL service ID | O | Identity of the VAL service.
VAL Server Id | M | Identify the VAL server for which the service experience report is sent
Timestamp | O | Time stamp of the collected report
VAL service experience report | O | Information related to VAL service experience. It may include end-to-end response time, connection bandwidth, request rate, VAL server availability, etc.
The ASM client sends Push service experience request to the ASM server. The request contains service experience report about a VAL server (e.g. end-to-end response time as experienced by client, connection bandwidth, request rate by client, VAL server availability, etc) and includes the VAL UE ID, VAL service ID, VAL server identity for which the report is being sent and time stamp of the report.
Push service experience report procedure in TR 23.700-97
Push service experience report procedure in TR 23.700-36

## Slide 6: Comparison - Procedures
Observation #4: Pull service experience report procedure is defined in both TR 23.700-36 and 23.700-97, where the client shares similar information to the server.
The ASM client sends the Pull service experience response to the ASM server. The response contains result indicating whether the report is available or not. If report is available, the response contains service experience report about a VAL server (e.g. end-to-end response time as experienced by client, connection bandwidth, request rate by client, VAL server availability, etc) and includes the VAL UE ID, VAL service ID, VAL server identity for which the report is being sent and time stamp of the report.
Pull service experience report procedure in TR 23.700-97
Pull service experience report procedure in TR 23.700-36
Information element | Status | Description
Result | M | Indicates whether the report is available or not
VAL UE ID | M | Identity of the VAL UE
VAL service ID (NOTE) | O | Identity of the VAL service.
VAL Server Id | M | Identify the VAL server for which the service experience report is sent
Timestamp (NOTE) | O | Time stamp of the collected report
VAL service experience report (NOTE) | O | Information related to VAL service experience. It may include end-to-end response time, connection bandwidth, request rate, VAL server availability, etc.
NOTE: These IEs are included only if the result is success. |  | 

## Slide 7: Comparison (Differences in both solutions)
Solution #1: Application Service Management Service (of FS_ACE_IOT)
  Following more procedures are defined
    Configuring VAL server (EN is present)
    Requesting for on-demand status
    Determines corrective action
    Subscribe – Notify Model
Solution #5: Service experience to support application performance analytics (of FS_ADAES)
  Following more procedures are defined
    Service experience information based on triggers
Observation #5: Both solutions have some extra procedures – however those procedures are related to the overall solution.

## Slide 8: Proposal for normative work
It is beneficial to define single SEAL service that handles both the solutions
  New SEAL server for application Service Management Service as studied in TR 23.700-97 can be merged in ADAE service.
It is proposed to specify both solutions (as per the agreed conclusions) under SEAL ADAE service and modify the scope of the ADAE service accordingly.
How to do this?
  Step 1: Bring Solution #5 from TR 23.700-36 to normative work in TS 23.436
    See S6-230230
  Step 2: Provide solution updates to bring remaining aspects of Solution#1 from TR 23.700-97