## Slide 1: ECS and ECS-ER
Intel, <supporters>

## Slide 2: ECS and ECS-ER
ECS provides
  EEC provisioning, support for registration functionality for EES etc.
One or more ECS can be deployed to support an EDN
On or more ECS can be deployed by a PLMN operator or ECSP.
ECS-ER is required to provide
  ECS Registration, ECS Discovery, EDN configuration retrieval etc. to support federation and roaming.
  ECS-ER needs to provide the ‘separation of concerns’ as required by GSMA i.e. provide separate interfaces for EWBI.
One ECS-ER can be deployed per ECSP, or one for multiple ECSPs, or by an MNO for all ECSPs.

## Slide 3: A Deployment view
ECS are required to register with ECS-ER.
  ECS-ER will need to support different/additional Information Schema than ECS (e.g. additional IEs to identify ECS within different EDNs).
ECS can not be dynamically upgraded/promoted as ECS-ER and vice versa
  To be pre-configured as ECS-ER
EDN-1
EDN-2
ECS
ECS
ECS-ER
EDN-3
ECS
ECS
EES
ECS-ER
OP-B
OP-A
ECS-ER needs to be designated and configured across the Operator Platforms
  The discovery of ECS-ER across platforms is not possible.
The scope and purpose of ECS-ER is different from ECS
  ECS-ER are providing support for federation and roaming.
  ECS-ER needs to identify each ECS registered with it.
EES
EES
EES
EES

## Slide 4: An Alignment view with ETSI MEC
Case-1: If ECS-ER is visualized as a special purpose ECS:
Case-2: IF ECS-ER as a functional superset of ECS
ECS
ECS-ER
MEC Federator
ECS-ER
ECS
MEC Federator
Both cases Do Not correctly represent ECS-ER role as federator and its alignment with MEC Federator.
Also clearly represents the overlap of functionalities and hence defy the GSMA requirement of “Separation of Concern’.
ECS
ECS-ER
MEC Federator
Case-3: ECS-ER as an independent architectural entity
Aligns Correctly with MEC Federator
Does not overlap the functional concerns – in line with GSMA views

## Slide 5: Conclusion
ECS-ER is a separate architectural entity.
  ECS-ER provides additional functionalities such as ECS registration etc.
  ECS-ER is an enhanced ECS because some of its functionalities are same as ECS (e.g. EDN configuration etc.)
    There can optionally be a new interface (EDGE-10’) defined between ECS and ECS-ER [To be decided] ?
ECS-ER aligns with MEC Federator.
  Needs to provide EWBI interface (EDGE-18).
  Interconnects with ECS using EDGE-10.
  As enhanced ECS – Will follow the same interface with other architectural blocks (e.g. EDGE-8’ etc.) – But this is implementation specific.

## Slide 6
Thank You !