## Slide 1: Application layer architecture update Discussion
Shao Weixiang (ZTE)

## Slide 2: Industrial automation communication structure
5G-ACIA WI021 Integration of Industrial Ethernet Networks with 5G Networks
The current industrial communications scenarios, ERP/MES/SCADA are factory IT systems through controllers/master (C/M) to manage OT product line devices include sensors and actuators (S/A).
Communication between L2/L3 infrastructure is predominantly wired.

## Slide 3: Transformation of industrial networks from Industry 3.0 to Industry 4.0
The Industry 3.0 automation pyramid focused on high throughput and very efficient machines, including dedicated networks.
IT domain include ERP/MES/SCADA
OT domain include Control/PLC, Field/IO
For Industry 4.0 factories, 5G can help for wireless.
5G device can integrate or replace with OT equipments such as Control/PLC, Field devices.

## Slide 4: Industrial automation communication with 5G

## Slide 5
5G-ACIA WI039- Exposure of 5G Capabilities for Connected
Industries and Automation Applications

## Slide 6: 5G-ACIA WI062- Exposure of 5G capabilities to industrial applications - architecture and protocol aspects
Exposure of 5G networks to IIoT Applications, where the IIoT Application is the service consumer and the 5G system the service provider.
En1 stands for the interface to access management related functions;
En2 stands for the interface to access SEAL exposure
En3 stands for the interface to access NEF exposure
Ed stands for the reference point allowing an IIoT Application running on the device to access to 5G network services

## Slide 7: 5G-ACIA WI062- Exposure of 5G capabilities to industrial applications - architecture and protocol aspects
For SEAL exposure
En2 interface corresponds to the SEAL-S reference point.
SEAL service enabler clients are situated in the 5G exposure function in the UE, and the Ed reference point therefore includes the SEAL-C reference point.
SEAL-UU defines internal interactions between the SEAL client and the SEAL server over the user plane.
The VAL client corresponds to the IIoT Application in the Industrial 5G Device and the VAL server corresponds to the IIoT Application in the IT Enterprise Domain.

## Slide 8: SEAL arch
Generic on-network functional model
Generic off-network functional model
VAL: Vertical Application Layer
Vertical application: An application catering to a specific vertical.
VAL UE: A UE that can be used to participate in one or more VAL services.
VAL client: An entity that provides the client side functionalities corresponding to the vertical applications.
VAL server: A generic name for the server application function of a specific VAL service.

## Slide 9: FFAPP old Arch is not right
It is confused for FF application specific layer and FAE layer, which are conflicated with VAL
In factory, OTA(over the top) do not directly connect bottom terminal side
Only need VAL server/client for FF

## Slide 10: FFAPP new Arch
In the factory, there are three layers which include Upper layer, FF application layer and OT layer.
The Upper layer include factory IT systems (e.g. ERP, MES, SCADA, etc) and/or 5G service provider Network Operations Center (NOC).
The OT layer include OT industrial devices, e.g. machine, robot, field devices, sensors, actuators, etc.
The FF application layer include FF UE and FF application server.
The FF application server consists of the FF VAL server, the SEAL servers.
The FF UE consist of the FF VAL client, the SEAL clients.

## Slide 11: FFAPP new Arch map to industrial networks
Upper layer
FF application server integrate or replace
FF UE integrate or gateway

## Slide 12: Thank You!