## Slide 1: VAL Service Area – comments and clarifications
Arunprasath R (arun.prasath@samsung.com)
Samsung

## Slide 2: Outline
VAL service Area – Same content as in S6-222782
Current use of location information - Same content as in S6-222782
Using VAL service area ID - Same content as in S6-222782
Comments and clarifications – (New Slides 7 to 12)
Summary - Same content as in S6-222782

## Slide 3: VAL Service Area
Interpretation of Location means different to different entities depending upon the context. For example, for a consumer, location is invariably civic address. For Network, it is one of Tracking Area/Routing Area (TA/RA), eNODEB ID, Cell ID. For a Vertical Application Layer (VAL), it can refer to the jurisdictional area of service.
Every vertical application server will have an area defined within which it provides the required service to the VAL users.
VAL service area can be defined through geographical co-ordinates and can be assigned an ID (VAL service Area ID)

## Slide 4: Current use of location information
Currently the VAL servers share the geographical area with the SEAL servers for the following :
  Get UE Information request from VAL server to SEAL LM server to get the list of UEs in a particular geographical area
  Location area monitoring subscription request from VAL server to SEAL LM to get the list of UEs as and when they move in or out of a particular location
  Location based group creation request from VAL server to SEAL GM to create a group with the list of UEs in a particular geographical area
In all the above cases the VAL server can share the VAL service Area ID as attribute instead of sharing the geographical co-ordinates.

## Slide 5: Using VAL service area ID
VAL server can register with the SEAL service the list of VAL service areas and the corresponding VAL service area IDs. This can happen only once and whenever there is a change in the VAL service area.
SEAL server maintains the mapping between the VAL service area (Geographical area) and the corresponding VAL service area ID.
Once the mapping/configuration of VAL service area and VAL service area ID is created the VAL server and SEAL servers can talk using the VAL service Area IDs instead of the location co-ordinates.
More than one VAL service area can be registered by the VAL server based on the VAL administration input.

## Slide 6: Using VAL service area ID
Once the VAL service area ID mapping is created, VAL server/SEAL servers can use the VAL service area IDs in the following :
  Location Report and location information notification from SEAL LM to VAL server can carry the VAL service Area ID in addition to location information. SEAL server can add the VAL service area ID corresponding to the location information
  GET UE(s) information request can carry the VAL service area ID instead of the geographical co-ordinates
  Monitor location subscription request can carry the VAL service Area IDs as areas of interest.
  Location area monitoring subscription request can include the VAL service Area ID as location information criteria
  Location based group creation
  Location based group update

## Slide 7: Comments and Clarifications
It is not clear the benefit (the benefit mentioned in P7 is the solution itself, rather than compared with the existing mechanism) to have this concept/solution. What are the drawbacks of using currently directly geographical information? Can you provide some vertical applications have special area define except using the civic/geographical address
  Here the proposal is to use the VAL service area instead of using geographical co-ordinates. VAL service creates the mapping of VAL service area ID and corresponding geographical coordinates.
  Once this mapping is created by the VAL service, instead of passing the geographical co-ordinates only the VAL service area Ids is provided by the VAL servers.
  Benefit here is the ease of use/management of service areas using the VAL service area Ids. We are not getting rid of the usage of civic/geogrphical co-ordinates. These are still used while creating the mapping of VAL service area Ids. VAL service area Ids will be dereferenced to the civic/geographical/network location co-ordinates.
  Every VAL will have service areas defined by the VAL administrator and through this proposal we are enabling the VAL admin to create mapping and name them through VAL service area Ids. E.g., First responders will have the responisbility areas defined, Electrictiy companies will have substation areas, health centers will have wards and each country will have different terminologies for verticals related to government services

## Slide 8: Comments and Clarifications
Only adding those IE in the information flow table does not make the solution complete. For example, what information is in the LMS to enable such information response ?
  LMS is configured by the VAL service with the mapping of location information and the VAL service area ID. Refer 9.3.2.x in the CR XXXX on how this mapping is created.
  Once this configuration/mapping is created, VAL service area IDs can be used in the information flows b/w VAL server and LMS. Also please note that the information element related to VAL service area ID is optional and not mandatory.

## Slide 9: Comments and Clarifications
From the business point of view, if the vertical application have such special area topology, whether it is the core business assets and shall not expose to others ?
  VAL service area ID is not considered core business assets. Its just the mapping of the location co-ordinates with a unique ID related to the VAL service. There is no harm in exposing the VAL service area IDs to SEAL layer.
The proposal appears to add complexity. For instance geographical information would still need to be shared by the VAL server, but with the introduction of an ID there would be the overhead of maintaining that ID, e.g., allocation management of the ID.
  We don’t see a complexity here. It is just maintaining the mapping of location co-ordinates and the corresponding VAL service IDs for each of the VAL services being served by the SEAL layer. Whole purpose of SEAL is to offload the complexity from the VAL layer and SEAL layer is handling more core logic and this mapping would not create any complexity IMHO.

## Slide 10: Comments and Clarifications
The proposal appears to add complexity. For instance geographical information would still need to be shared by the VAL server, but with the introduction of an ID there would be the overhead of maintaining that ID, e.g., allocation management of the ID.
  We don’t see a complexity here. It is just maintaining the mapping of location co-ordinates and the corresponding VAL service IDs for each of the VAL services being served by the SEAL layer. Whole purpose of SEAL is to offload the complexity from the VAL layer and SEAL layer is handling more core logic and this mapping would not create any complexity IMHO.

## Slide 11: Comments and Clarifications
It is not clear what would be the format of such service area - is it going to be a number?
  It is a unique string identifier.
What are the drawbacks of using currently directly geographical information?
  No drawbacks as such but usage of VAL service area ID brings in more flexibility and ease of management of the functionalities involving location information. Below are some of the functionalities which requires location information and can be replaced with VAL service area IDs:
    To obtain UE(s) information in an application defined range of location
    Monitor the VAL UE’s location in a given area of interest
    Monitor the list of UEs moving in or moving out of the specific location area
    Updates subscription to location area monitoring
    Location based group creation
    Location reporting triggering criteria

## Slide 12: Comments and Clarifications
Benefits/Advantages of VAL service area ID is not clear in the usage of subscriptions
  Lets take the case of VAL server1 has created a mapping VALServiceArea1 with a specific location co-ordinates
  VAL server1 has used the VALServiceArea1 in the APIs related to the functionalities listed in the previous slide
  Now the VAL admin changes the VALServer1’s service area. If the communication b/w VAL and SEAL had happened using the VAL Service Area ID as in this proposal, the VAL server just need to update the VALServiceArea1 with the new/updated location co-ordinates.
  It doesn’t have to invoke individual APIs to update the location co-ordinates of its interest. SEAL layer internally takes care of the updates on receiving the new configuration for the VAL Service Area ID
  All SEAL entities starts applying the new location co-ordinates without explicit request from VAL:
    SEAL GM starts updating the group membership based on the updated VAL service area ID
    SEAL LM starts applying the new co-ordinates for triggering criteria, monitor location subscription, location area monitoring subscription

## Slide 13: Summary
In summary usage of VAL service Area ID brings in more flexibility when using or consuming the functionality from SEAL involving location information.
VAL service area ID can be shared across the SEAL servers and any change/update in the VAL service area can be easily managed. When there is change / update in VAL service Area, then VAL server can just update the VAL service area at SEAL domain only once and need not update its subscription to various APIs where location information is utilized.
                THANK YOU