## Slide 1: Updates to 23.222 to enable stage 3 CAPIF extensions
Nokia, Apple, Intel, Huawei

## Slide 2: Background
In LS S6-222714, ETSI ISG MEC has requested 3GPP to add a protocol-level extensibility mechanism.
SA6 has indicated to be positive about the request and to elaborate on the necessary stage 2 changes.
This discussion paper describes the needed extensions and motivates a proposed way forward for the stage 2. Please see S6-223199 containing a CR0096 against TS 23.222 (Rel-18).

## Slide 3: MEC Requirement 1: Extensible enums
"Allow ETSI ISG MEC to extend enumerations, e.g., for data formats, protocols and security mechanisms, without breaking "native" CAPIF API invokers."
CAPIF so far only supports the HTTP protocol. Goal: add more protocols to the published / discoverable service API descriptions.
Same for data formats (only JSON supported) and security mechanisms (which are related to the protocols).
Ensure that extended information will not confuse "native" CAPIF implementations.

## Slide 4: MEC Requirement 2: Extension containers
"Support extension containers that would allow an "extended" CAPIF AEF to provide additional information […] during service API publication, persist such extension containers by CAPIF and return them as part of the discover service APIs result."
External SDO defines additional service attributes to describe REST extensions or alternative API architectures e.g. RPC, message bus.
In the API publication request, such additional extension attributes need to be carried ("tagged and bagged") in “extension containers”.
Subsequently, the actual content of "extension containers" is stored by the CCF
In the API discovery response, the "extension containers" with their content are provided back to the API invoker.
If extensions are defined by an external entity, these extension attributes would need to use the 3GPP defined "extension container" mechanism. If defined by 3GPP, these extensions can be built directly into the data model.

## Slide 5: MEC Requirement 3: Extensible queries
"Provide a mechanism that allows definition of additional filtering criteria for discover service API queries."
Some of the information attributes in an extension container may also be needed as search criteria during the "Discover service APIs" procedure
This enables specifying "API invoker's interest" (as in Req. [AR-4.2.2-b]) also in terms of information originating from data model extensions.

## Slide 6: Way forward
ETSI ISG MEC requests protocol level extensions for publish and discover
  Minimal changes, no need for prior study
Suggest to update 23.222 Rel.18 to enable CT3, SA3 and MEC to move ahead with defining the necessary protocol-level extensions
  Add an extensibility requirement to clause 4.2 "Service API publish and discover" to cover the MEC requirements 1-3
  Mention data model extensions in the related information flows in clauses 8.x
  Open up clause 9.2 "Fundamental API Guidelines" and 9.3 "Architecture design considerations" to allow including non-REST API architectures (for instance, allow "API endpoints" in addition to "resources")

## Slide 7: BACKUP

## Slide 8: Illustration of possible protocol-level extensions (*)
(*) illustrative only, the actual development is entirely in scope of 3GPP CT3
Extensions
extension container -> persist content on registration, return content on discovery
filter extension hook -> use attributes from extension container in GET queries
extensions of enums (protocols, data formats) -> allow signalling of other protocols and data formats
security extension container -> allow signalling of security information e.g. related to "alternative" protocols used by MEC
Legend
blue – extension points
1 exactly one
? zero or one
+ one or more
* zero or more