## Slide 1: Discussion on “UE ID” vs “Edge UE ID”
Shahram Mohajeri (AT&T)

## Slide 2: Problem statement
23.558 specification needs further clarification regarding:
  UE ID definition
  UE ID relationship with 5GC’s AF-specific UE ID
  UE ID vs Edge UE ID vs AF-specific UE ID
  Which system generates the AF-specific UE ID (e.g. EEL or 3GPP 5GC)
Lack of clarity of the spec leads to misinterpretation in the industry

## Slide 3: Rel-17 EDGEAPP definition of UE ID & usage
“UE ID” definition (23.558 clause 7.2.6):
  “The UE ID uniquely identifies a particular UE within a PLMN domain”
“UE Identifier API” states (23.558 clause 8.6.5.1):
  “EES exposes UE Identifier API to the EAS in order to provide an identifier uniquely identifying a UE… The UE ID is specific to the given EAS and it is represented as a GPSI assigned by the 3GPP Core Network”
UE ID is used over EAS-EES APIs such as:
    Location API , Session with QoS API, AC information exposure API (i.e. notifications from EES to EAS)
UE ID used over EEC-EES and EEC-ECS APIs such as:
    Service provisioning request, EEC registration, EAS discovery request
Key Point: “UE Identifier API” returns “EAS-specific UE ID” assigned by 3GPP core network

## Slide 4: Rel-18 EDGEAPP Study uses the term “Edge UE ID”
Appearance of “Edge UE ID” for the first time in Solution #23 “UE identification with NAT”
  Solution #23 tries to address the fact that when NAT is deployed, Nnef_UEId_Get service (invoked by EES) fails as it cannot find the UE’s IP address known by the underlying 3GPP network
  Solution #23 employs EEC instead which uses private IP address (as known by the 3GPP network) to invoke Nnef_UEId_Get service via EES
Reason for solution #23: Since EAS invocation of “UE Identifier API“ failed, EAS uses AC/EEC path to retrieve the needed UE Identifier!
“Edge UE ID” name was used to really mean “EAS-specific UE ID”
Key Point: regardless of which path EAS uses to retrieve the UE ID, it has to be the same (i.e. “EAS-specific UE ID” assigned by 3GPP core network as per “UE Identifier API” (23.558 clause 8.6.5.1))

## Slide 5: AF-specific UE ID and the problem it’s addressing
UE ID which is a GPSI by definition, can either be in the form of a MSISDN or an External-ID
  If for privacy reasons the user doesn’t want to share MSISDN with the AF, then the AF may ask NEF for an External-ID form of the GPSI:
    AF uses the External-ID over API requests towards NEF
    3GPP network notifies AF of subscribed events using External-ID towards NEF
  Hence, by definition, GPSI in the form of an External-ID is meant to protect user’s privacy
Additionally, in order to ensure user’s privacy is not compromised across AFs, the Nnef_UEId_Get service returns AF-specific UE ID (i.e. no two AFs get the same UE ID for a given UE)
Key Point: By definition, the “AF-specific UE ID” provided by the 3GPP network is an anonymous privacy-protecting UE Identifier

## Slide 6: Stage 3 defined Eees_UEIdentifier_Get procedure
According to 29.559 procedure (see excerpt below) the UserInformation provided by EAS in the request is used to invoke Nnef_UEId service. That is:
  In step 3a: there is no indication that EES uses its own AFId (as opposed to what EASId) in its Nnef_UEId call to NEF. Also (as shown in bold, it derives DNN/S-NSSAI based on EASId)
  In step 3b: there is no indication of mapping the NEF provided UE ID to EES’s produced “Edge UE Id” to be sent to EAS in the response
With no indication (in stage 2 and 3 specs) that there is a need for mapping to take place in EES (from EASId to EESId and vice versa in the invocation of Nnef_UEId service), one would correctly take the spec to mean that, EAS-specific UE ID is provided by the NEF and EES just passes that up to EAS without any additional mapping.

## Slide 7: Summary
EAS, regardless of using EES directly or indirectly through AC/EEC to retrieve the UE ID, must receive the same response
  that is “EAS-specific UE ID” as provided by the 3GPP network
EAS may use EDGE-3 or EDGE-7 for API invocation (or receive notifications) pertaining to a UE which is identified anonymously by “EAS-specific UE ID” as provided by 3GPP network
“Edge UE ID” generated by EEL, doesn’t provide any added value while introducing unnecessary complexity
Key Point: There is no need for the “Edge UE ID” as the “AF-specific UE ID” is already a privacy-protecting UE Identity plus allowing EAS, if needed, to also use it in its communication with 3GPP network directly over EDGE-7

## Slide 8: Way forward –Step 1
Consistent with the existing 23.558 spec as well as the stage 3 specified (29.558) UE ID retrieval procedure, it is recommended to continue the usage of the term “UE ID”
  i.e. Do not introduce the term “Edge UE ID”
    The corresponding contributions S6-230567 (i.e. Revision of S6-230462 – agreed to in #52-bis-e) recommending the required changes to S6-230462 is submitted to this meeting
Clarify the “UE ID” definition in 23.558 in order to show its relationship with 23.502’s “AF-specific UE ID”
  The corresponding contributions, S6-230566, recommending the required changes is submitted to this meeting

## Slide 9: Way forward –Step 2
Send an LS to SA2/SA3 and cc CT3 in order to validate the existing Eees_UEIdentifier_Get procedure as defined in 23.558 & 29.558 where EES uses the AFId of the EAS received (as opposed to its own AFId; see highlighted description from NEF API spec) in its call onto Nnef_UEId service.
  If SA2/SA3 response required changes to the defined procedures in 23.558 & 23.559, then SA6 would take necessary steps to update 23.558 for Rel-17 & Rel-18 accordingly
A draft LS (S6-230568) is submitted to this meeting
29.522: Nnef_UEId call