## Slide 1: Addressing EN in cl.10.6.3.3 in TS 23.280
Rana Alhalaseh
Ericsson, Nokia, Nokia Shanghai Bell, AT&T

## Slide 2: Outline
Problem statement
Observations to consider
Way forward

## Slide 3: Problem statement
- Ref. TS 23.280
- Ref. TS 23.280
Notes: The partner Mc system needs to be aware of the migration status of migrated users; whether they are available at that system or not
The primary MC system is always aware via migration service authorization procedure which partner MC system the migrated user is at

## Slide 4: Problem statement
Step 11: The partner MC service server stores the necessary information related to the migrated MC service user (e.g., MC service ID of the migrated MC service user provided by the primary MC system mapped to the MC service ID of the migrated MC service user provided by partner MC system). The migration status of the MC service user allows proper communication redirection back to the primary MC system once the migrated MC service user is no longer migrated on this partner MC system.
Editor's note: How the partner MC system gets informed that the MC service client no longer receives MC services from that partner MC system is FFS.
- Ref. TS 23.280
Notes: Allow proper routing of communication via the redirection towards the partner or primary system

## Slide 5: Observations to consider
Editor's note: How the partner MC system gets informed that the MC service client no longer receives MC services from that partner MC system is FFS.
It is irrelevant to the partner MC system whether the migrated user is heading (i.e., migrating) to another third partner MC system or is returning back to its primary MC system – transparent solution to the user`s direction is needed
The migrated user does not request (no request/response) to migrate out from the partner MC system. This is under the control of the primary MC system
The partner MC system just needs to be informed or notified that the migrated user is no longer present
This information should not be provided as part of a request/response procedure, if it fails there is an issue in subsequent steps and potential failure in migrating to another partner system or returning back to a primary system

## Slide 6: Observations to consider
Editor's note: How the partner MC system gets informed that the MC service client no longer receives MC services from that partner MC system is FFS.
This notification should be sent by the primary MC system, since it is the only entity to be aware and to control which MC system its user is present in – MC user returns back to the primary MC system or migrates to a third partner MC system: all happen via the primary MC system
The migration status of an MC user at the partner MC system is binary information (receives or does not receive MC services from that partner MC system). The MC service IDs mapping information is stored but not cleared. The period how long to keep the mapping information is left to implementation.
While migrating out from a partner MC system into (another partner/its primary) MC system, there is no guarantee that the (was-migrated) MC user still has access to that partner system from which the MC service user is migrating out, nor is able to receive communication via its MC service ID provided by that MC system

## Slide 7: Way forward
Step 13-15: As the MC service user has been migrated at the partner MC system B earlier, the primary MC service server A sends a migration service de-authorization notification to the partner MC server B via their gateway servers.
Note 4: The MC service server A is able to send migrated service de-authorization notification as well towards the MC service server B via their respective gateway servers in the scenario once the MC service clients migrates out of MC system B and returns back to the primary MC system A. This can happen after the MC service client has finalized the User Authentication and Authorization procedures defined in 3GPP TS 33.180.
Step 15: The MC system B updates the MC service user’s migration status accordingly and keeps the mapping of its assigned MC service ID by partner MC system B with the MC service user`s MC service ID assigned by its primary MC system A to allow proper redirection of services via the primary MC service server A, as described in clause 10.16.5.