## Slide 1: Identities behind MC GW UE cl.11.3 in TS 23.280
Rana Alhalaseh
Ericsson

## Slide 2: Outline
Highlight some concepts from 11.2 and 11.3
Questions and discussion
Proposal for way forward

## Slide 3: MC GW UE functional model cl.11.2.0
Figure 11.2.0-1: Functional architecture
For non-3GPP devices which can host an MC client, the MC gateway UE enables connectivity to the MC server. For non-3GPP devices which cannot host the MC client, the MC gateway UE hosts the instantiation of the MC client for the non-3GPP device.
  Observation 1: Non-3GPP devices which can host a client need to have a SIP client with SIP credentials.
  Observation 2: Non-3GPP devices which cannot host a client does not have SIP identities, therefore, they rely on the MC GW client
IMPU: IP Multimedia PUblic identity
IMPI: IP Multimedia Private Identity

## Slide 4: MC GW UE functional model cl.11.2.0
The MC gateway UE provides MC service capabilities and 3GPP access capabilities using 3GPP network credentials for authorized access with an MC server.
For non-3GPP devices which cannot host MC clients, the MC gateway UE shall control the access and manage the communication between the non-3GPP devices and the MC server. Upon reception of connection authorization request from a non-3GPP device, the MC gateway UE instantiates an MC client, acting on behalf of the non-3GPP device, to provide the requested services (e.g. emergency call, group calls, short data messages services, etc.). The communication interworking and the definition of associated procedures between the MC client (initiated at the MC gateway UE) and the non-3GPP devices is out of scope of this document.
NOTE 1: MC clients residing on a non-3GPP device cannot use UICC credentials to perform authorisation with the 3GPP transport system.
For MC clients getting MC service access via the MC gateway UE, the MC gateway UE forwards (unmodified) signalling and media from the individual MC clients to the MC server and vice versa.

## Slide 5: Identities behind the MC GW UE cl.11.3
11.3.1 General
The MC gateway UE enables access to the MC system for MC service clients either hosted on the MC gateway UE or hosted on non-3GPP devices using non-3GPP connectivity with the MC gateway UE. Simultaneous sharing of an MC gateway UE by multiple MC service clients requires a unique relationship between the MC service identities used by the MC service clients with corresponding media streams passing the MC gateway UE towards the MC system sharing 3GPP connectivity of the MC gateway UE.
A MC service user behind the MC gateway UE has no 3GPP transport access credentials (i.e., no UICC), whereas the MC system relies on private user identity associated with public user identities (i.e., IMPUs/IMPIs) needed for authentication purposes. Moreover, the one-to-one correspondence between MC service ID and IMPUs enables routing of signalling traffic between the MC service server and the MC service client.
Observation 3: this one-to-one restriction needs to be revisited for the case when non-3GPP devices cannot host a client.
IMPU: IP Multimedia PUblic identity
IMPI: IP Multimedia Private Identity
Notes: To identify users behind MC GW UE we need them to have unique IMPU/IMPI, and each has a unique MC service ID.

## Slide 6: Identities behind the MC GW UE cl.11.3
11.3.2 When using separate IMS subscriptions
If the MC service clients are hosted by non-3GPP devices or the MC service clients are hosted by the MC gateway UE, an MC service user corresponding to an MC client uses a dedicated IMS/SIP subscription without any relation to the MC gateway UE subscription.
Figure 11.3.2-1 depicts the use of the IMS Credential (IMC) application in accordance with 3GPP TS 23.228 [9].
Observation 4: this is aligned with the fact that each client (not instantiation clients for non-3GPP devices which cannot host one) has its unique IMPU, and each mapped to a unique MC service ID (cl. 11.3.1) irrespective whether IMS subscription is separate or shared. Furthermore, based on Frame route (cl. 11.4) signaling for each client, e.g., SIP registration can be done separately.
Observation 5: Figure 11.3.2-1 implies that IMS subscription is considered all the time for the case when non-3GPP devices can host a client.
Figure 11.3.2-1: Using separate IMS subscriptions

## Slide 7: Identities behind the MC GW UE cl.11.3
11.3.3 When sharing MC gateway UE's IMS subscription
The MC service clients rely on MC service IDs provided by the MC gateway UE. In this case, the MC service clients behind the MC gateway UE share the credentials from the IMS subscription of the MC gateway UE, as shown in Figure 11.3.3-1. The number of MC service clients behind the MC gateway UE is determined by the number of subscribed MC service IDs that are associated with the IMS subscription of the MC gateway UE.
Observation 6: there is no MC service clients behind MC GW UE in Fig. 11.3.3-1. The client for non-3GPP device which cannot host a client is an instantiation within the MC GW UE. This is not aligned with the highlighted text in green.
Observation 7: There is no IMPI/IMPU for 3GPP devices which cannot host a client. 3GPP has no related information.
Observation 8: The green highlighted text in cl. 11.3.3 contradicts figure 11.3.3-1.
Figure 11.3.3-1: Sharing the MC gateway UE's IMS subscription

## Slide 8: Questions and discussion
What identities can be provided to identify users behind MC GW UE in this case?
  No IMPU/IMPI identities for users which cannot host a client
How to achieve one-to-one correspondence between MC service ID and IMPU for user resides on non-3GPP device which cannot host a client?
What binding/ mapping is present in MC server per user resides on non-3GPP devices which cannot host a client.
Notes: What identities under 3GPP’s control in the case when non-3GPP devices cannot host a client?
  3GPP has no authorities to identify identities or credentials of non-3gpp devices that cannot host a client. The communication between the initiated MC client at the MC gateway UE and the non-3gpp devices is out of scope of 3GPP.

## Slide 9: Questions and discussion
Figure 5.1.1-1: MCX authentication and authorization – ref. TS 33.180
How to perform SIP registration for users at non-3PP devices which cannot host a client?
B-1: SIP registration and authentication
  Either via SIP REGISTER or SIP PUBLISH, cl. 7.3.2 and 7.3.3 in 3GPP Ts 24.379
  The SIP registration is identified via IMPU
  If service authorization is successful, the MC service server stores the binding of the MCPTT ID and MC service client ID to the IMPU, as per cl. 7.3.2 and 7.3.3 in 3GPP Ts 24.379

## Slide 10: Proposal for way forward
Proposal 1: agree on the difference between “identities behind MC GW UE” vs “users behind MC GW UE”.
  There is no identities behind the MC GW UE for the case when supporting non-3GPP devices which cannot host a client. There is no identities for 3GPP to control, there are users for MC GW UE to provide MC access for.
Proposal 2: relax the restriction in cl. 11.3.3: “the one-to-one correspondence between MC service ID and IMPUs enables routing of signalling traffic between the MC service server and the MC service client.”
  This restriction is valid in all cases except for the case of non-3GPP devices which cannot host a client, as they do not have IMS identities.
Proposal 3: combine cl 11.3.2 and 11.3.3, since each MC client (not instantiation clients for non-3GPP devices which cannot host one) has its unique IMPU, and each mapped to a unique MC service ID (cl. 11.3.1) irrespective whether IMS subscription is separate or shared. Furthermore, based on Frame route (cl. 11.4) signaling for each client, e.g., SIP registration can be done separately.