## Slide 1: Constrained and Unconstrained Devices
Jerry Shih, at&t
jerry.shih@att.com

## Slide 2: Definitions?
In our TS 23.554, there are no definitions but with examples in clause 4.2.2:
  [AR-4.2.2-a] MSGin5G UE:
    1) constrained devices (e.g. sensors, actuators) and
    2) unconstrained devices with advanced capabilities (e.g. washing machine, micro-ovens)
[AR-4.2.2-b] The application architecture shall enable the unconstrained devices to act as a UE Message Gateway to constrained devices to communicate with MSGin5G Server.

## Slide 3: CISO Platform
The constrained devices are end nodes with sensors/actuators that can handle a specific application purpose. They are usually connected to gateway-like devices, low power lossy network, and in-turn communicates with the IoT cloud platforms. Typically they communicate via low power wireless protocols like BLE, 802.15.4 (6LoWPAN, Zigbee, Thread, WirelessHART etc), LPWAN etc and mostly battery powered with low data rate.
The constraints of these devices are
  Code complexity (ROM/Flash), Size of state and buffers (RAM)
  Processing power
  Available power source and that has limits on reachability over time, if battery powered.
  User interface and accessibility in deployment
  Bitrate/Throughput
  Highly asymmetric link characteristics
  Cost
  Physical size
  CISO: Social Network Exclusively for Senior Security Professionals to Learn & Collaborate

## Slide 4: More definitions
Nothing from Wikipedia
A device that has limited processing and storage capabilities, and that often runs on batteries (IGI Global)
A constrained device has significantly reduced CPU power, memory, connectivity, or energy availability compared to a server or traditional API client machine.

## Slide 5: RFC 7228 Constrained-Node Network
Small devices with limited CPU, memory, and power resources, so called "constrained devices" (often used as sensors/actuators, smart objects, or smart devices) can form a network, becoming "constrained nodes" in that network. Such a network may itself exhibit constraints, e.g., with unreliable or lossy channels, limited and unpredictable bandwidth, and a highly dynamic topology.
Constrained devices might be in charge of gathering information in diverse settings, including natural ecosystems, buildings, and factories, and sending the information to one or more server stations. They might also act on information, by performing some physical action, including displaying it. Constrained devices may work under severe resource constraints such as limited battery and computing power, little memory, and insufficient wireless bandwidth and ability to communicate; these constraints often exacerbate each other. Other entities on the network, e.g., a base station or controlling server, might have more computational and communication resources and could support the interaction between the constrained devices and applications in more traditional networks.
Today, diverse sizes of constrained devices with different resources and capabilities are becoming connected. Mobile personal gadgets, building-automation devices, cellular phones, machine-to-machine (M2M) devices, and other devices benefit from interacting with other "things" nearby or somewhere in the Internet. With this, the Internet of Things (IoT) becomes a reality, built up out of uniquely identifiable and addressable objects (things). Over the next decade, this could grow to large numbers [FIFTY-BILLION] of Internet-connected constrained devices, greatly increasing the Internet’s size and scope.

## Slide 6: RFC 7228 Class of Constrained Devices
Class 0 devices are very constrained sensor-like motes. They are so severely constrained in memory and processing capabilities that most likely they will not have the resources required to communicate directly with the Internet
Class 1 devices are quite constrained in code space and processing
capabilities, such that they cannot easily talk to other Internet
nodes employing a full protocol stack such as using HTTP, Transport
Layer Security (TLS), and related security protocols and XML-based
data representations.
Class 2 devices are less constrained and fundamentally capable of
supporting most of the same protocol stacks as used on notebooks or
servers.

## Slide 7: Examples of constrained devices

## Slide 8: Reference points
5.4.6 MSGin5G-5
  The interactions related to enabling MSGin5G message related information exchange between an Application Client and an MSGin5G Client are supported by the MSGin5G-5 reference point. This reference point supports:
  Providing information from Application Clients required to enable the MSGin5G Client to construct an MSGin5G message to be delivered to other MSGin5G Service endpoints.
  Configuring application clients with information required to enable the MSGin5G Client and MSGin5G Server to exchange and route MSGin5G messages to other MSGin5G Service endpoints.
  Sending notifications and information in the incoming MSGin5G messages received by the MSGin5G Client to the Application Clients from other MSGin5G Service endpoints.
5.4.7 MSGin5G-6
  The MSGin5G Client of MSGin5G UE-2 communicates
  with MSGin5G Client of MSGin5G UE-1 over
  MSGin5G-6 reference point. The interface is based on NR PC5.

## Slide 9: The related clauses
5.3.3 MSGin5G Client
  MSGin5G Client acting as a relay for MSGin5G Client resides in other UE, which does not have enough capability to communicate with MSGin5G Server (i.e. a constrained device), to use MSGin5G Service.
  NOTE 2: An MSGin5G Client residing in a constrained device is the same as an MSGin5G Client residing in an unconstrained device. I.E. both of them use the same transport/data formats and have the same capabilities.
8.1.4 MSGin5G UE bulk configuration over MSGin5G-6 reference point
8.2.7 MSGin5G UE bulk registration over MSGin5G-6 reference point
8.2.8 Constrained device selecting MSGin5G Relay UE or MSGin5G Proxy UE
8.11 Constrained devices in MSGin5G Service
  8.11.2 Constrained device registration to use gateway UE
  8.11.3 Constrained device Deregistration from using gateway UE
  8.11.4 Constrained device sending message using Gateway UE
  8.11.5 Constrained device receiving message via Gateway UE

## Slide 10: Still not clear
What does a constrained device in our application layer protocol mean? Different transport over MSGin5G-5 and MSGin5G-6?
Should we avoid the use of constrained devices which are so hardware/physical capabilities related.
8.11 procedures are all back-to-back gateway cases (over MSGin5G-5 reference point)
  Why only Application Client on UE-2 (8.11.2) needs to register with the MCGin5G Client on UE-1 to get MSGin5G services not the Application Client within UE-1
  Same for sending and receiving messages
We are missing the relay cases over MSGin5G-6 reference point?

## Slide 11: Mission Critical model
Function Model of MC gateway UE media plane
Functional model of MC gateway UE signalling plane

## Slide 12: Summary
Should we follow the Mission Critical model and not use confusing constrained device concept?
The focus in our development is a messaging service that allow (mainly) IoT devices to exchange messages:
  The ecosystem is supported by MSGin5G Client, MSGin5G Server and Gateway Servers that forms the foundation of how the messages can be exchanged for our use cases.
  Applications leverage a messaging ecosystem to exchange the messages is a norm today, from SMS, RCS, What’s App, Messenger, LINE to WeChat etc. Applications are all different and beyond anyone’s imagination; they cannot be standardized.
  A simple and well-defined messaging ecosystem is much more useful than a clumsy defined messaging ecosystem with imaginary applications; wrong focus.
  There should be only one type of device in MSGin5G service, the MSGin5G UE with the MSGin5G Client that supports the service; all other types of devices are non-MSGin5G devices and will be supported by a gateway function (be it a server or a MSGin5G UE) to access to the MSGin5G Server.
  Applications should be defined in its own trade association and only come to MSGin5G development with clear user/architectural requirements that benefits to all potential usages of the messaging ecosystem. Application specific needs should only be handled in the applications, not to comprise the whole ecosystem.

## Slide 13: Additional Slide on call models (if discussion is needed)

## Slide 14: Simple call models on MSGin5G Server