## Slide 1
Discussion on MSGin5G Proxy UE, MSGin5G Relay UE and MSGin5G Gateway UE
Yue Liu (China Mobile)
S6-230694

## Slide 2: Gateway UE, Proxy UE and Relay UE
MSGin5G UE-1 can be act as Gateway UE, Proxy UE and Relay UE as per the current definition in TS23.554
MSGin5G Gateway UE: an MSGin5G UE which constructs and sends MSGin5G message upon receiving request along with required application specific data from the Application Client on the Constrained UE (without MSGin5G Client). The same MSGin5G UE can also deliver the received MSGin5G message towards the target Application Client on the Constrained UE (without MSGin5G Client).
MSGin5G Proxy UE: an MSGin5G UE which constructs and sends MSGin5G message upon receiving MSGin5G message from the MSGin5G Client on the Constrained UE. The same MSGin5G UE can also deliver the received MSGin5G message towards the target MSGin5G Client on the Constrained UE.
MSGin5G Relay UE: an MSGin5G UE which receives MSGin5G message from Constrained UE (with MSGin5G client) and forwards it to the MSGin5G Server and vice-versa.

## Slide 3
 | A Party | B Party | Application layer functionalities | Use cases
MSGin5G Gateway UE | Application Client | MSGin5G Server | Receives application request Builds new MSGin5G message | Constrained UE without MSGin5G Client
MSGin5G Proxy UE | MSGin5G Client | MSGin5G Server | Receives MSGin5G message Builds new MSGin5G message Changes the information included in the MSGin5G message | Bulk registration Segmentation/reassembly when supported segmentation size of constrained UE is different message (de-)aggregation
MSGin5G Relay UE | MSGin5G Client | MSGin5G Server | Forwards the MSGin5G message with no modification | 
Comparison of current definitions

## Slide 4
Option 1:keep Proxy UE (rename it as Gateway UE) and Relay UE, remove (existing) Gateway UE.
    Gateway UE (new) used in bulk configuration/registration.
    Relay UE used in other messaging scenarios. The constrained UE exchanges messages with Proxy UE by using ProSe L2 or L3 relay. The Relay use case can be left to ProSe since the MSGin5G Client in the middle do nothing.
    constrained UE without MSGin5G Client is out of scope and leave to implementation
Option 2: keep Proxy UE (for constrained UE with MSGin5G Client, provide all MSGin5G Relay/Proxy features) and Gateway UE (for constrained UE without MSGin5G Client)
    The Proxy UE (including the current Proxy UE and Relay UE) uses back-to-back mechanism, creates a new MSGin5G message based on received MSGin5G message
    The Gateway UE is responsible for the translation between application request (API provided by MSGin5G Client in the middle) and MSGin5G message.
    The constrained UE with MSGin5G Client exchanges MSGin5G messages with Proxy UE by using ProSe Direction communication (UE-UE). ProSe UE-to-Network Relay can not be used.
    The Relay use case can be left to ProSe since the MSGin5G Client in the middle do nothing.
New classification of MSGin5G UE in the middle

## Slide 5
Option 3: keep Relay UE and Gateway UE, bulk configuration/registration is not supported.
    The definition of Relay UE and Gateway UE are not needed to be changed
    Bulk configuration/registration is not supported
    The Relay use case can be left to ProSe since the MSGin5G Client in the middle do nothing.
Option 4: Remove all the constrained UE scenarios
    Constrained UE without MSGin5G Client and bulk configuration/registration are out of scope
    Leave relay feature to ProSe.
New classification of MSGin5G UE in the middle

## Slide 6
 | Type of UE in the middle | Supported features | Removed features | Lower layer transport between constrained UE and UE in the middle
Option 1 | Gateway UE (new) Relay UE | Message exchange between constrained UE with MSGin5G Client and MSGin5G Server Bulk configuration/registration | constrained UE without MSGin5G Client | Gateway UE: ProSe UE-UE Relay UE: ProSe UE-network relay
Option 2 | Gateway UE, Proxy UE (new) | Message exchange between constrained UE with MSGin5G Client and MSGin5G Server Bulk configuration/registration constrained UE without MSGin5G Client | none | ProSe UE-UE
Option 3 | Gateway UE, Relay UE | Message exchange between constrained UE with MSGin5G Client and MSGin5G Server constrained UE without MSGin5G Client | Bulk configuration/registration | Gateway UE: ProSe UE-UE Relay UE: ProSe UE-network relay
Option 4 | none | Message exchange between constrained UE with MSGin5G Client and MSGin5G Server (leave to ProSe) | constrained UE without MSGin5G Client Bulk configuration/registration | ProSe UE-network relay
Comparison among the options

## Slide 7: Conclusions and proposals
Option 2 is more clear and fulfills all existing features. It is proposed to use Option 2 to modify the definitions and related procedures.
  If the constrained UE communicates with the MSGin5G Client in the middle via MSGin5G-5 reference point, the MSGin5G Client in the middle acts as MSGin5G Gateway UE.
    The constrained UE exchanges MSGin5G messages with Gateway UE by using ProSe Direction communication (UE-UE). ProSe UE-to-Network Relay can not be used.
    The Proxy UE builds new MSGin5G message based on received application request via MSGin5G-5 reference point. (similar in the other direction)
  If the constrained UE communicates with the MSGin5G Client in the middle via MSGin5G-6 reference point, the MSGin5G Client in the middle acts as MSGin5G Proxy UE.
    The constrained UE exchanges MSGin5G messages with Proxy UE by using ProSe Direction communication (UE-UE). ProSe UE-to-Network Relay can not be used.
    The Proxy UE builds new MSGin5G message based on received MSGin5G message via MSGin5G-6 reference point. (similar in the other direction)
The definition of MSGin5G Relay UE can be removed. The related procedures are needed to be re-written by using MSGin5G Proxy UE.