## Slide 1
Discussion on SF and deferred delivery
Yue Liu (China Mobile)
S6-230698

## Slide 2: Simple call models in MSGin5G Server

## Slide 3: Requirement of message delivery assurance
3GPP TS22.262
[R-5.1.2-005] The MSGin5G Service shall support storage of a message if a UE is unavailable (disconnected or power off) for future delivery once the UE becomes available.
The stage 1 requirement is about the message delivery assurance but may cause misunderstanding since the example in the requirement may have different meaning with “unavailable”.
What we have in the current TS23.554 is Store and than Forward the MSGin5G message based on the availability. The availability is indicated by registration status and (if registered) the Communications Availability IE (e.g. Scheduled communication time, Communication duration time etc) in the MSGin5G Client Profile
What we miss in the current TS23,.554 is the delivery assurance when the recipient is registered but unreachable, e.g. disconnected or power off as required by TS22.262. Therefore, deferred delivery is needed.
Both Store and than Forward and deferred delivery are processed by the MSGin5G Server in the terminating side since only it knows the registration status and the reachability of the recipient.

## Slide 4: Service logic of the MSGin5G Server when both S/F and deferred delivery are introduced

## Slide 5
Conclusion and proposals
Update the S/F procedure specified in clause 8.3.6.
Add a new clause 8.3.7 to specify the deferred delivery procedure.
Add a new clause 8.0 (maybe next meeting?) to cover the overall procedure of message delivery, e.g. divide the end-to-end procedure into originating procedure and terminating procedure, add the service logic of MSGin5G Client and MSGin5G Server to specify how to use the procedures listed in the clause 8.