## Slide 1: Discussion about QoS guarantee by switching SEALDD server
Niranth (namogh@huawei.com)
Jian Zhang (zhangjian369@huawei.com)
Huawei, Hisilicon

## Slide 2
Background
In KI#3 about supporting for data transmission quality measurement and guarantee, the following issue is described:
The HW contribution proposes that transmission quality can be guaranteed by switching SEALDD server:
How to support data transmission in SEALDD enabler layer with guaranteed quality?
Before switching SEALDD server: UE#1/SEALDD client#1 <--> RAN#1 <--> ULCL <--> UPF#1 <--> SEALDD server #1 <--> VAL server (the transmission quality cannot be satisfied)
After switching SEALDD server: UE#1/SEALDD client#1 <--> RAN#1 <--> <--> ULCL <--> UPF#1 or UPF#2 <--> SEALDD server #2 <--> VAL server (the transmission quality can be satisfied, by changing N9 and/or N6 interface)

## Slide 3
QoS guarantee by switching SEALDD server
RAN#1
UPF#1
UPF#2
SEALDD
Server#1
SEALDD
Server#2
SEALDD
Server#3
VAL
Server#1
VAL
Server#2
VAL
Server#3
N9
N9
N6
N6
N6
ULCL
N3
SEALDD client#1
UE#1
For case#1: By switching SEALDD server to solve bad N6 and/or overload issue
For case#2: By switching both UPF and SEALDD server to solve bad N9 issue
Pre-condition:
S-SEALDD server (e.g. SEALDD server#1) can detect the transmission quality suffering from deteriorated QoS, and can diagnose the issue caused by N6/load (case#1) or N9 (case#2)
Aggregation Router
Aggregation Router

## Slide 4
QoS detection and diagnose issue
QoS detection:
Diagnose issue:
The S-SEALDD server can detect the QoS deterioration based on the E2E transmission quality measurement (i.e., UE---RAN—UPF--SEALDD server) procedure in clause 9.7
QoS monitoring procedure supports the transmission quality measurement between UE and RAN, or between UE and UPF
Based on the E2E transmission report from SEALDD server, and QoS monitoring between UE and UPF, S-SEALDD server can diagnose the bad N6/overload issue
Based on the E2E transmission report from SEALDD server, and QoS monitoring between UE and RAN, S-SEALDD server can diagnose the bad N9 issue

## Slide 5: Summary
This contribution proposes to QoS guarantee by switching SEALDD server, including:
The SEALDD server switching can be triggered based on the transmission quality report (from itself) and the QoS monitoring (from 5GS)
The SEALDD server can diagnose the deteriorated QoS issue caused by bad N6 or SEALDD overload, or by bad N9
By switching the SEALDD server and/or UPF, the QoS requirements of VAL application can be satisfied