## Slide 1: Discussion on potential packet loss during multicast MBS delivery and solutions
Cuili Ge, Yanmei Yang
Huawei, Hisilicon, Hytera

## Slide 2
5GC
Phase 1: MCX AS create/activate a multicast MBS session, and start to deliver group communication media via the multicast MBS session to the joined MCX UE.
The NG-RAN support MBS and shared delivery is applied. The shared delivery toward NG-RAN is triggered by the 1st joined UE per 7.2.1 in TS 23.247.
MCX AS
Potential packet loss when using multicast MBS
Multicast MBS
- active
UL media
Joined & CM-CONNECTED
5GC
MCX AS
Multicast MBS
- inactive
UL media
Joined & CM-IDLE
Phase 2: No one talks in the group for a while.
The multicast MBS becomes inactive, and some UEs enter IDLE mode due to no media transmission
5GC
MCX AS
Multicast MBS
- active
UL media
Phase 3: User A talks again.
The multicast MBS becomes active due to new media packet is coming.
The idled UE is being page. The UEs will become connected again.
But, these UE may not become connected at the same time. The late connected UE may lost the media packet , as the packet already being transmitted once the 1st UE become connected which triggers the shared delivery restore and start transmit data again.
Packet is lost !!!
All is caused due to the MC service server is NOT aware of the multicast session status changes.
Joined & CM-CONNECTED
Joined & CM-IDLE

## Slide 3
Which happened if packet loss occurs?
When packet loss happens during the speech packet transmission, the late users may miss the important information from the talker.
When the packet loss happens during the application level signaling, e.g, in pre-established MBS case, the late connected users will miss e.g., the call request/GroupMapToSession, and unable to join the call or receive the following media via MBS. This is not acceptable.

## Slide 4
Potential solutions
Options | Brief description | issue
A – within SA6 | Repeat the application level signaling several times over the multicast MBS | Burden to the server and UE to handle the extra packet/message; Cost extra network transmission resources.
B – SA6 and SA2 | Activate the multicast when the multicast MBS is in inactive status | Request SA2 to provide the multicast MBS inactive status to SA6 MCX server, similar as cl. 7.3.5 for broadcast session status in TS 23.247 Compared with Option A, this one has the lowest cost of network resource, and processing resource at the server and UE.

## Slide 5
Proposals
For Rel-18, SA6 prefer to adopt option C, the reasons are as follows:
  Option C only requires minor enhancement/changes to SA2.
  in SA6, Option C only optionally need one more step - MBS activation step before sending the media if the session is inactive now. (Cl. 7.3.3.4.2 in 23.289, only cover the case that the MCX initially create the multicast MBS session and set inactive state.)
It is proposed to agree the related CR, and send LS to SA2 for the multicast MBS session status exposure.
Figure 7.3.3.5.2-1: MC service group media transmission over MBS sessions
Optionally, if the MBS session is inactive, MC service server activates the multicast MBS session as described in TS 23.247
New step

## Slide 6
Thanks