## Slide 1: SA6#53 external TR (exTR) – Working Procedure and Contributions
Intel, Apple, China Mobile, ??

## Slide 2: External TR (exTR) Scope*
Alignment and Deployment Aspects of EDGEAPP with ETSI MEC and GSMA OP
  Alignment will include
    EAS profile (EDGEAPP) and AppInfo (ETSI MEC)
    Alignment of EDGE-3 and Mp1 reference points (mapping of IEs and APIs)
    Alignment of EDGE-9 and Mp3 (Mp3 specs (IEs/APIs) do not exist, so no alignment is required!)
    Usage of CAPIF between the two architectures
    Deployment Options
      Co-existence of two architectures
        Coexistence of EES and MEC Platforms
  Alignment may include
      End to End deployment options
      Aspects related to Federation & Roaming
* Based upon WID (S6-221496)

## Slide 3: Contributions for exTR
Inviting contributions to external TR (exTR)
  exTR is a recommendation from 3GPP to external bodies, developers and other organizations.
Contributions to exTR based upon agreed contributions from Normative discussions
  Technical aspects needs agreement during normative discussions and captured in TS.
Contributions to exTR based upon the Technical Studies
  Informative content with no architecture/procedural impact – to avoid duplicate content in TS.

## Slide 4: Recommendations
During exTR development: Any content to be captured in both TS and external TR preferably be captured through simultaneous contributions (CR for TS 23.558 as well as pCR for exTR 23.958)
During external TR Change Control: Any content to be captured in both TS and external TR shall be captured through simultaneous contributions (Two CRs for TS 23.558 and 23.958 respectively)
Agreed informative content with respect to alignment (with no architecture/procedural impact) in EDGEAPP TR can be captured only in exTR.
  This will avoid duplicated content in TS and avoid any confusion later between TS and exTR contents.
  Capture the alignment aspects as agreed for KI#5 in the TR on
    Alignment of EDGE-3/Mp1, EASProfile/AppInfo, EDGE-9/Mp3
    Any other scenario based upon further discussion and agreement in SA6!

## Slide 5: Thank You!