## Slide 1: Introduce Non-3GPP direct IP connection for fused location service in TS 23.434
Liping Wu, Chunshan Xiong
CATT

## Slide 2: Outline
Why we need “non-3GPP direct IP connection” ?
Introduce “non-3GPP direct IP connection”
Benefit for introducing “non-3GPP direct IP connection”
Proposal

## Slide 3: Why we need “non-3GPP direct IP connection” ?
  The SEAL Location Management architecture introduced the UE location information could be obtained over 3GPP access (e.g. NR and LTE) based on the SEAL LM architecture as defined in clause 9 of TS 23.434 V18.3.0.
The 5G FLS WI is agreed to use different kinds of location access types to get UE location information from more sources to further improve the LCS QoS (e.g. accuracy, latency).
According to TS 23.402 and TS 23.501, the UE location information could be obtained over the non-3GPP access connecting to EPC or 5GC, however it is not enough. As using the non-3GPP access without traversing the EPC or 5GC(we call/define it “non-3GPP direct IP connection” between LM client and LM server) is also a good option to get the UE location information.
The “non-3GPP direct IP connection” could provide an additional IP connection to let UE to route traffic data without traversing the 5GC which can fulfil and further improve the 5GFLS LCS QoS [pls refer more information in slide 5].
NOTE: Non-seamless WLAN offload function as defined in clause 5.42 of TS 23.501 and clause 4.1.5 of TS 23.402 is one type of “non-3GPP direct IP connection”.

## Slide 4: Introduce “non-3GPP direct IP connection” for fused location service in TS 23.434
In order to fulfil and improve the LCS QoS for the 5GFLS WI, the “non-3GPP direct IP connection” is proposed for the SEAL Location Management architecture of TS 23.434(as described in Figure 3).
  LM Client can additionally or alternatively provide UE location information data to LM Server via the “non-3GPP direct IP connection” without traversing the 3GPP core network. E.g. The LM Client of UE can use WiFi or wireline to directly connect to the LM Server without e.g. UPF to improve the reliability and reduce the latency of the location service.
Figure1-UE location information is obtained over 3GPP access (e.g. NR,LTE) as described in TS 23.434
Figure2-UE location information is obtained over accesses including the non-3GPP access traversing the EPC or 5GC, which suggested by CR#0173 (S6-230973)
Figure3-UE location information is obtained over accesses including the non-3GPP access without traversing the EPC or 5GC

## Slide 5: Benefit for introducing “non-3GPP direct IP connection”
It is proposed to introduce the “non-3GPP direct IP connection” in SEAL Location Management architecture for the 5GFLS WI into TS 23.434, because it can:
  Provide additional IP path for the UE to increase the network connection reliability and bandwidth.
  Provide low latency than that of the non-3GPP access traversing EPC/5GC.
  Be much cheaper and much easier to be deployed for the customers/operators.
  Provide larger scope and be more available in some usage than 3GPP access.
  Be any available IP connection, not just the “Non-seamless WLAN offload” as defined in TS23.501.

## Slide 6: Proposal
Considering the above analyses, it is proposed to endorse the following proposals:
  Introduce the “non-3GPP direct IP connection” between the LMC of UE and the SEAL Location Management Server for the 5GFLS into TS 23.434.
  Define another new reference point instead of “LM-UU” to support “non-3GPP direct IP connection” in clause 9.2.5 of TS 23.434.
  Update CR#0173 (S6-230973) of TS 23.434. Although the non-3GPP access is introduced in the CR, however it focuses on the non-3GPP access connecting 5GC/EPC, the non-3GPP access without traversing 3GPP core network is not included.

## Slide 7
Thanks

## Slide 8: Different Access types are introduced to meet the LCS QoS
In order to meet the LCS QoS requirements, different kinds of access type and positioning methods are introduced in TS 29.572.
However, no matter what the access type is, the traffic data flows should get through the 5GC or EPC.
UE Reporting Access Type in Clause of 6.1.6.3.17 of TS 29.572
Positioning Methods in Clause of 6.1.6.3.6 of TS 29.572
Notes: Benefit of introducing non-3GPP system as user plane option. SA6 is working on application layer, why user plane selection is needed by AF and how?
- If needed, why this is particular for SEAL LM, not for SEAL, EDGEAPP and other enablers? And what are impacts on system level?

## Slide 9: UE support Non-seamless WLAN offload
UE also support Non-seamless WLAN offload as defined in clause 5.42 of TS 23.501 without traversing the 5GC to fulfil the LCS QoS requirement.
It’s necessary to introduce the similar function for LMC of VAL UE in SEAL LMS function model of TS 23.243.
Notes: The partner Mc system needs to be aware of the migration status of migrated users; whether they are available at that system or not
The primary MC system is always aware via migration service authorization procedure which partner MC system the migrated user is at