## Slide 1: Binding restrictions for MC GW UE in TS 23.280
Rana Alhalaseh
Ericsson

## Slide 2: Outline
Observations and problem statement
Questions for discussion
Proposal for way forward

## Slide 3: Observations and problem statement
Authorized binding (association) between MC GW UE and MC GW client is essential step to provide MC access to MC users behind MC GW UE.
Authorize MC service users on non-3GPP devices can/cannot host an MC service client.
The MC service server is aware of the unique IP address of the MC service users behind the MC GW UE for resources requirement (QoS).
Clause 11.2 Functional Model
If the MC service user on the non-3GPP device utilizes multiple MC services simultaneously, the MC service access may also be provided by one or multiple MC gateway UEs as shown in figure 11.2.0-2 while restricting each MC service to one MC gateway UE (e.g. MCPTT via MC gateway UE1, MCData via MC gateway UE2).

## Slide 4: 11.5.1.2 Connection authorisation for non-3GPP devices that host an MC client
11.5.1.2.3 Connection authorisation procedure
Step 4: The MC server performs an authorization check, to verify that access via the MC gateway UE is permitted. An MC server shall reject the connection authorization when the MC server receives connection authorization from a MC gateway client for a particular MC service for which the connection already exists with the same or different MC gateway UE.
Figure 11.5.1.2.3-1: Connection authorisation with an MC server via an MC gateway UE

## Slide 5: 11.5.1.3 Connection authorisation for non-3GPP devices that do not host an MC client
11.5.1.3.3 Connection authorisation procedure
Step 2: The MC server performs an authorization check, to verify that access using the MC gateway UE is permitted. An MC server shall reject the connection authorization when the MC server receives connection authorization from a MC gateway client for a particular MC service for which the connection already exists with the same or different MC gateway UE.
Figure 11.5.1.3.3-1: Connection authorisation of an MC gateway client hosted by an MC gateway UE

## Slide 6: MC GW switching
Observation 1: When the non-3GPP device is triggered to switch from MC GW UE 1 to MC GW UE 2, authorization binding procedure must be done towards MC GW UE 2 (break-before-make). As a result, the MC user on non-3GPP device may suffer MC service interruption (may suffer packet drop).
Observation 2: In case the MC gateway client has lost the connection, i.e., the authorized binding towards the MC gateway UE without a proper disconnection procedure, the MC service server may not be aware of this update. Hence, it may reject any reattempted authorization binding procedure by the MC gateway client.
MC server
(e.g. MCPTT server)
MC gateway UE1
(using MC service capabilities)
MC client
non
-
3GPP
access
3GPP access
non
-
3GPP device
(E.g., can host MC clients)
MC gateway UE2
(using MC service capabilities)
Currently: one MC access per MC GW UE at a time

## Slide 7: Questions for discussion
How to prevent the MC service users behind the MC GW UE from suffering service interruption (packet loss) due to break- before- make?
  How to consider make-before-break approach?
Currently, if the MC service user has lost the connection to its associated MC GW UE without a proper discussion procedure, the MC service user is unable to reconnect to any MC GW UE, since the MC service server will reject any authentication.
  How to solve this issue?
Proposal 1: the MC service server controls the active binding between the MC GW client and multiple MC GW UEs per MC service.
The limit of number of devices an MC GW UE can support is up to implementation.

## Slide 8: Proposal 2: 11.5.1.2 Connection authorisation for non-3GPP devices that host an MC client
11.5.1.2.3 Connection authorisation procedure
Step 4: The MC server performs an authorization check, to verify that access via the MC gateway UE is permitted. An MC server shall may reject the connection authorization when the MC server receives connection authorization from a MC gateway client for a particular MC service for which the connection already exists with the same or different MC gateway UE.
Figure 11.5.1.2.3-1: Connection authorisation with an MC server via an MC gateway UE

## Slide 9: Proposal 3: 11.5.1.3 Connection authorisation for non-3GPP devices that do not host an MC client
11.5.1.3.3 Connection authorisation procedure
Step 2: The MC server performs an authorization check, to verify that access using the MC gateway UE is permitted. An MC server shall may reject the connection authorization when the MC server receives connection authorization from a MC gateway client for a particular MC service for which the connection already exists with the same or different MC gateway UE.
Figure 11.5.1.3.3-1: Connection authorisation of an MC gateway client hosted by an MC gateway UE