## Slide 1: Discussion on Integrated Sensing and Communication related work in SA6
Cuili Ge, Yanmei Yang
Huawei, Hisilicon

## Slide 2
SA1 progress on Integrated Sensing and Communication
Rel-19
FS_Sensing - Study on Integrated Sensing and Communication 950003
2022/3/10 - 2023/6/6
SA1 Integrated Sensing and Communication study:
Scope/Objective：
  UC - enhancement of the 5G system to provide sensing services addressing different target verticals/applications, e.g. autonomous/assisted driving, V2X, UAVs, 3D map reconstruction, smart city, smart home, factories, healthcare, maritime sector.
  RAT - focus on NR-based sensing, while some use cases might make use of information already available in EPC and E-UTRA without impacts on EPC and E-UTRA.
  Sensing - collecting and reporting of sensing information, sensing related KPIs. Security, privacy, regulation and charging are additional topics of concern.
Progress
  TR refers to 32 scenarios, covering 5 verticals：Smart transportation, UAV, Smart living, Smart city, Smart factory.
  Defined 3GPP sensing data，N3GPP sensing data and Sensing result.
  Now is 80% completion.
  The scenarios and requirements are almost stable, the next work is consolidation work.
 It is time to consider how to start the sensing work in SA6, especially dealing with the relationship with SA2

## Slide 3
Use cases and business model with ASP
5G system assisted automotive maneuvering/navigation
Vehicles Sensing for ADAS
Pedestrian/animal intrusion detection
V2X UC example
UAV flight trajectory tracing by 5G system
Network assisted collision avoidance for UAVs
Sensing for UAV intrusion detection
UAV UC example
Sensing People or obstacles detection in smart factory
AGV presence and proximity detection
Smart factory UC example
APP
MNO
Core network
RAN
Network sensing APIs
UE
Verticals
Exposure data:
3GPP sensing data
Sensing result
Make use of 3GPP sensing data/sensing result into their application functions
Consumer
Sensing service producer
The 3GPP network will provide network sensing API with 3GPP sensing data/Sensing result to the ASP.

## Slide 4
Related work in SA6
Related working task | Any dependency with other groups/work
1、 Identify the use cases already been enabled by SA6, which needs to be enhanced with sensing. Also identify new UC/verticals need sensing can be enabled by SA6 with sensing | Stable SA1 use case and requirement
2、Identify when & where to make use of the network sensing capabilities | Stable SA1 use case and requirement
3、Further processing of 3GPP sensing data/Sensing result from network, and provide value-added service API to VAL service | SA2 network sensing API exposure
Proposal
SA6 can firstly start WT1 and WT2
Partially start WT3, and complete WT3 with the stable SA2 network sensing API exposure