## Slide 1: Introduction of non-3GPP system for application
Wenliang Xu (Ericsson)
S6-231372

## Slide 2: Background
TS 23.434 v18.4.0 has the following EN in SEAL LM:
  Editors Note: The need for a new reference point or extending the existing reference point for the non-3GPP defined network system is FFS
Currently, SA6 specified functions for vertical application (e.g. EdgeApp, Vertical application enablers) are based on 3GPP system (i.e. 3GPP UE, RAN and CN).
TS 23.282 specified that certain application functions of MCData service can be accessed using MCData UEs via non-3GPP access network.
TS 23.280 and 23.379 specified that certain MC service functions such as dispatch and administrative functions could also be supported via non-3GPP access networks but no additional functionality is specified to support non-3GPP access.
3GPP SA2 specified architecture to support Non-3GPP access includes trusted and untrusted non-3GPP access network and wireline access network (see TS 23.501, cl.4.2.8).

## Slide 3: Non-3GPP access connected to 3GPP CN
Regardless of the access network type, UPF/P-GW in 3GPP CN is used in user plane.
3GPP UE
3GPP RAN
Non-3GPP AN
3GPP CN
SEAL servers
CR S6-230973 introduce the non-3GPP access network connected to 3GPP CN for SEAL.

## Slide 4: Non-3GPP system
3GPP UE
WLAN AN
3GPP CN
SEAL servers
One example is 5G NSWO defined in TS 23.501. The 5GC is only used for authentication (still the UE is a 3GPP UE), and the application traffic is sent in user plane btw. UE and SEAL servers via WLAN AN).
If UE is a non-3GPP UE and SEAL client in the UE talks with SEAL servers via a non-3GPP transport network, user plane connectivity is out of 3GPP scope (e.g. LAN deployed by enterprise).
Non-3GPP UE
Non-3GPP TN
SEAL servers

## Slide 5: Aspects need study and coordination
Introducing non-3GPP system like NSWO as application information transport is not a particular topic for 5GFLS WI, it should be discussed in a wider scope in SA6, possibly looping other groups like SA4.
A rough investigation on non-3GPP system shows some challenges:
  For instance, the NWSO was introduced mainly to offload traffics that are low-revenue and large volume for MNO. For SEAL-Uu signaling (e.g. LM-Uu message), it doesn’t fall into that characteristics.
  Exposure capabilities offered by 3GPP system are specified by SA2, especially for location retrieval, the 3GPP CN is an important data source. Can non-3GPP system support the same?
  For reliability and bandwidth consideration, so far it is not clear how SA2 can support redundancy and ATSSS between 3GPP system and non-3GPP system.
  Security.

## Slide 6: Possible way forward
Suggest to agree “non-3GPP access with 3GPP CN” as originally proposed in S6-230973 (rev: S6-231371).
SA6 is near to the end of Rel-18, the“non-3GPP access w/o using 3GPP CN” needs holistic consideration and coordination with other SA groups. If needed, a Rel-19 study item can be triggered.