## Slide 1: Common EAS issues
Catalina Mladin
Convida Wireless

## Slide 2: Use of announced info in discovery [issue 5]
Issue 5: using announced common EAS information (e.g. from EES 1 to EES 2) in discovery at EES 2. Our issue with the use of the announced information is that the announced EAS belongs to EES 1. By allowing discovery of an EAS of EES 2 via EES 2 affects EAS-EES cardinality/ principle. While the cardinality says that an EAS can TALK to a single EES, based on rel-17 an EAS can be discovered only through EES 1. This change can profoundly impact regular discovery, ACR, etc. It is an important architectural change done stealthily (I consider cardinality part of architecture).. Rather it should be explicit and its impact on other procedures should be clearly stated.
[Yajie]: it is based on the Sol#31, maybe Basu could make further clarification and provide the clarification.
Cnv Proposed WF: EN about addressing this later, while keeping the announcement (see S6-231382)
S6-231284 improves this, but CR option removed, so alignment still needed.

## Slide 3: Common EAS info store [issue 4]
Issue 4: Edge architecture principle is that EAS info is maintained at EES, EES info at ECS. This means that the association between Common EAS and group ID is maintained at EES, the association between common EES and group ID is maintained at ECS/ ECS+CR. Current CR has a couple of places where the association between common EAS ID and group ID is pushed to ECS. In addition, this is a violation of an existing edge principle done stealthily, without clear description in text.
[Yajie]: it is based on the Sol#30, maybe Wenliang could make further clarification.
Cnv Proposed WF: S6-231284 changes this and CR option in general, so alignment still needed.

## Slide 4: Single EES choice w/ CR [issue 3]
Issue 3: restricting the ECS-CR supported case to a single EES choice made by ECS. The restriction is not warranted, and it makes the CR deployment choice quite useless, since maintaining a single (EES ID, group ID) mapping does not require a repository (It also doesn’t make sense because the CR support should offer more functionality, not less). In addition, this restricts EEC from making EES choices for itself, as it currently does.
[Yajie]: ECS+ER identify one or more EES as the CR mentioned.
Cnv Proposed WF: Based on email response this should be resolved. Just confirm at conf call, then make sure text is aligned.

## Slide 5: Providing aggregate KPIs [issue 2]
Issue 2: not adding “list of common EAS criteria” to the Application group profile. Here the Convida position is that it wants to support cases for which the KPIs needed for group support are very different than those for single member support. More info was provided in the exploder thread attached, which clarifies also that the functionality also helps predictive services about the EAS load. Supporting the usecase has no impact on the rest of this proposal, so we hope for compromise to support other company’s usecase.
[Yajie]: disagree with the multiple AC case and list of common EAS criteria. the reason I clarified in the previous meeting.
Cnv Proposed WF: Clarify why providing this info is an issue. The info is needed for predicting loads

## Slide 6: Support of multi AC ID usecase [issue 1]
Example, Tencent game PUBG publishes two ACs, one in Android, another in iOS.
In case that the UE is running mobile OS, the ACID is a pair of OSId and OSAppId.
OSid is different, OSappid can also be different or same. Anyway ACID used in Android Phone and iOS phone is different. […]
If one AC is designed in a way with multiple AC components and each component has different ACID, in the same UE (I have not seen such a design btw.), is this multiple ACs connecting to the same EAS covered by our solution? If different components are installed in different devices/UEs, they can be connected to the same EAS for consuming EAS service. Here I’m assuming the same EAS ID is used. […]
If we say different ACs need to talk with the same EAS and the same EAS is providing EAS ID service 1 to AC1 and EAS ID service 2 to AC2. And it is better to have one EAS to reduce latency in EAS-EAS communication. Well, this case can be further studied. Since they probably involves re-grouping operation (merge group1 and group2). At this point of time, such a need (if exists) can be done in R19.

## Slide 7: Existing IDs vs App group definitions
7.2.4 Edge Application Server ID (EASID)
  The EASID identifies a particular application for e.g. SA6Video, SA6Game etc. For example, all Edge SA6Video Servers will share the same EASID.
  NOTE: The definition of the EASID is out of scope of this specification.
7.2.5 Application Client ID (ACID)
  The ACID identifies the client side of a particular application, for e.g. SA6Video viewer, SA6MsgClient etc. For example, all SA6MsgClient clients will share the same ACID.
  In case that the UE is running mobile OS, the ACID is a pair of OSId and OSAppId.
Application Group ID uniquely identifies a group of UEs using the same application. It is allocated (either dynamically or pre-configured in the AC) by the ASP and is unique within the application