## Slide 1: What happens with unspecified IEs?
Peter Sanders
One2many (an Everbridge company)

## Slide 2: Outline
What happens with Information Elements that are defined at stage 2 in TS 23.554, but have
  no usage,
  no format
  no value range
Does stage 3 fix that?
  CT1: TS 24.538 (reference points MSGin5G-1)
  CT3: TS 29.538 (reference points MSGin5G-2/3/4/7)
Or does this lead to proprietary implementations?

## Slide 3: SA6 Architecture
Scope:
CT1
CT3

## Slide 4: Priority
SA6: [AR-4.1.2-e] The MSGin5G service should support different application priority levels for the MSGin5G messages including High, Normal and Low.
CT1: CT3:
"priority": {
"type": "string",
"enum": [
"HIGH",
"MIDDLE",
"LOW"
],
Priority:
anyOf:
- type: string
enum:
- HIGH
- MIDDLE
- LOW
- type: string
description: >
This string provides forward-compatibility with future
extensions to the enumeration but is not used to encode
content defined in the present version of this API.
Priority IE is missing from UEMessageDelivery

## Slide 5: Configuration
SA6:
CT1:
CT3:
  Configuration is not specified; Non-MSGin5G UE information is not supported

## Slide 6: Store and Forward
SA6:
CT1:
CT3:
Application specific S&F info is not specified at stage 3

## Slide 7: Registration (I)
SA6:
CT1: CT3: No registration specified at all for
non-MSGin5G UE, only for AS
List of port numbers and associated protocol is an unspecified string

## Slide 8: Registration (II)
SA6:
CT1: - Failure Cause not specified
- Failure Cause also missing from the de-registration response

## Slide 9: Registration (III)
SA6:
CT1: CT3: No registration specified for
non-MSGin5G UEs
- Date-time format is specified in RFC3339 and is not expressed as a number of seconds or minutes
- Data size is expressed as a string
- S&F opt-out is expressed as a string

## Slide 10: Summary
If stage 2 specifies IEs that have no usage, no format and no value range, don’t expect stage 3 to fix that.
  Stage 3 will either
    Specify a “string” for such IE, which will lead to proprietary vendor implementations, or
    Not specify the IE at all
Standards should ensure interoperability between systems of different vendors and should not lead to proprietary implementations that ensure interoperability problems or vendor lock-in.