## Slide 1: More on Constrained Devices
Jerry Shih, at&t
jerry.shih@att.com

## Slide 2: Definitions
Constrained UE definition:
  an MSGin5G UE which cannot connect to the 3GPP network directly for message exchange with MSGin5G Server.
Examples in clause 4.2.2:
  [AR-4.2.2-a] MSGin5G UE:
    1) constrained devices (e.g. sensors, actuators) and
    2) unconstrained devices with advanced capabilities (e.g. washing machine, micro-ovens)
  [AR-4.2.2-b] The application architecture shall enable the unconstrained devices to act as a UE Message Gateway to constrained devices to communicate with MSGin5G Server.
A NOTE 2 from 5.3.3.1 on MSGin5G Client
  NOTE 2: An MSGin5G Client residing in a constrained device is the same as an MSGin5G Client residing in an unconstrained device. i.e. both of them use the same transport/data formats and have the same capabilities.

## Slide 3: 5.2 Application Architecture
The architecture shown in Figure 5.2-2 and Figure 5.2-3 illustrate architectural options for providing MSGin5G services for constrained devices. In these figures, the MSGin5G UE-2 is a constrained device which does not connect to the 3GPP network directly for message exchange with MSGin5G Server (e.g. UE-2 is out of 3GPP RAN coverage, with or without authorization to use UE-to-Network relay). If allowed by configuration, the MSGin5G UE-2 can use the options listed below to communicate with the MSGin5G Server:
  the MSGin5G UE-2 uses an UE-1 as relay;
  the MSGin5G UE-2 interacts with an MSGin5G Gateway UE which supports MSGin5G Gateway Client.

## Slide 4: 5.3.3.2 MSGin5G Gateway Client
An MSGin5G Gateway Client is an MSGin5G Client which supports MSGin5G Gateway service functionality in additional to the MSGin5G Client functionalities specified in clause 5.3.3.1. It enables constrained devices to obtain services from the MSGin5G Server when communications via ProSe UE-to-Network Relay are not or cannot be supported.
The MSGin5G Gateway service functionality in the MSGin5G Gateway Client supports:
supporting the bulk configuration and bulk (de-)registration for the MSGin5G Client residing on the Constrained UE, e.g. checking whether bulk configuration/bulk (de-)registration can be used, holding the (de-)registration request from MSGin5G Client residing on the constrained device, construction of the bulk (de-)registration request and splits of the MSGin5G UE bulk (de-)registration response, etc.
Editor’s note: Whether other capabilities, e.g. detailing of the support for (de-)registration of constrained devices, are needed to be supported by MSGin5G Gateway service functionality is FFS

## Slide 5: 8.1.4 MSGin5G UE bulk configuration over MSGin5G-6 reference point
When constrained devices MSGin5G UE-2a and UE-2b, which support an MSGin5G Client, get the MSGin5G Service configuration information via MSGin5G UE-1, the MSGin5G UE-1 may decide to use bulk configuration procedure specified in this clause based on service policy.

## Slide 6: 8.2.8 Constrained device with MSGin5G Client selecting MSGin5G Gateway UE
The signalling flow for MSGin5G Client-2 in the MSGin5G UE-2 (which is a constrained device) to request other MSGin5G UEs supporting MSGin5G Gateway service functionality to provide their configuration is illustrated in figure 8.2.8-1.
Pre-condition:
1) MSGin5G UE-2 is not able to communicate with MSGin5G Server directly;
2) MSGin5G UE-2 discovers nearby MSGin5G UEs using ProSe direct discovery procedure as specified in 3GPP TS 23.304 [18].
3) An MSGin5G UE-3 supports MSGin5G Gateway service functionality (i.e. MSGin5G UE-3 is an MSGin5G Gateway UE) and an MSGin5G UE-1 does not support MSGin5G Gateway service functionality (i.e. MSGin5G UE-1 is not an MSGin5G Gateway UE).
Figure 8.2.8-1: Constrained UE sending message to request configuration of the MSGin5G Gateway UE

## Slide 7: Conclusion
The constrained device is the same as a regular MSGin5G UE when it supports MSGin5G client.
The MSGin5G Gateway UE is defined (used) to provide connectivity to MSGin5G Server (to get the MSGin5G services) when a MSGin5G UE is outside of coverage OR a UE without MSGin5G client.
If a UE doesn’t support MSGin5G client (as standalone) should it be supported in our spec?
We do support an Application Client to use a MSGin5G gateway UE to obtain MSGin5G services on a UE that doesn’t support MSGin5G Client, but it focuses on the Application Client connectivity to a MSGin5G Client (on the MSGin5G gateway UE) not the non MSGin5G UE.
Theoretically, a MSGin5G UE’s Application Client can also use a MSGin5G gateway UE to obtain MSGin5G services without using the MSGin5G Client on the same UE.
A constrained UE = a remote MSGin5G UE in the context of UE (not clients)?
  Should rename constrained UE to remote MSGin5G UE and its context (such as in [AR-4.2.2-b]) to avoid confusion and
  Remove the sub bullets of requirement 1 in clause 4.2.2.