## Slide 1: SA6 Rel-19: Discussion on Application Layer support for ATSSS (AL-ATSSS)
Lenovo
S6-232418

## Slide 2: Outline
Background
Motivation
Proposed Study
Potential Objectives

## Slide 3: Background
The Access Traffic Steering, Switching, Splitting (ATSSS) feature, as defined in TS 23.501 clause 5.32, enables data traffic to be exchanged between a UE and a UPF over multiple access paths.
Each access path may be using either 3GPP access (such as terrestrial or non-terrestrial NG-RAN) or non-3GPP access (such as WLAN).
In order to enable the ATSSS feature, an MA PDU Session must be established, and configure the UE and UPF with steering rules.
The steering policies are created by the PCF during the MA PDU Session establishment procedure and are employed by the SMF to create "ATSSS rules" for the UE and "Multi-Access Rules (MAR)" for the UPF.
The steering rules indicate how the traffic of the MA PDU Session should be distributed over the available access paths between the UE and the UPF.
Each steering rule contains a “steering functionality” (e.g. MPTCP, MPQUIC, ATSSS-LL) and a “steering mode” (e.g. load-balancing, active-standby, smallest-delay, redundant, etc.)
Simplified architecture of ATSSS as defined in the 3GPP specifications

## Slide 4: Motivation (1)
Consideration 1: Support for vertical tailored implementations
In SA2, when specifying ATSSS feature the ATSSS rules are provided at CN, without taking into account vertical/ASP requirements e.g. for providing steering rules. In some verticals (e.g. FF, V2X) , the vertical may need to be in control of the traffic steering/splitting/switching rules to allow for vertical-tailored ATSSS based on their requirements
Observation 1: SA6 functionality (which is about vertical service enablement within 3gpp system) may be required to support for translating the vertical requirements to ATSSS rules, given different vertical use cases and deployments
Consideration 2: Support for multiple access paths (multiple 3gpp and non-3gpp access paths)
Current ATSSS feature (as of Rel-18) supports multiple accesses for 1 3gpp access and 1 non 3gpp access. Based on Rel-19 DualSteer SA1 use cases, this may be needed to be extended to more access paths.
Observation 2: Assuming multiple 3gpp and non-3gpp paths, the application layer support for configuring and providing ATSSS rules is more prominent, since this may involve 3GPP access paths from multiple operators as well as non-3gpp accesses.
NOTE: SA6 functionality has already capabilities for multi-operator support which can be extended to support AL-ATSSS.

## Slide 5: Motivation (2)
Consideration 3: Enhance SA6 functionality for providing multi-access enablement services
In SA6, the utilization of multiple access technologies, including non-3gpp access was considered in SEAL as part of LMS, where the LMS can utilize both 3gpp and non-3gpp access paths to retrieve location information from the VAL UEs as well as external systems.
However, there is no reference point defined for non-3gpp access (not traversing 3gpp system); and further work would be expected to investigate such aspects.
New enablers which are being discussed as part of Rel-19 (e.g. AEXR) have as objective to support seamless session support (e.g. XR streaming) over 3GPP or non-3GPP access (e.g., device connecting to the 5G network directly or indirectly).
Observation 3: The study of the application layer support for ATSSS would be necessary and complementary to provide the framework for the steering/splitting/switching of application traffic for current and new enablers which may require the utilization of multiple accesses to support enablement services.

## Slide 6: Motivation (3)
Consideration 4: Implementation of ATSSS across the 3GPP core network
Implementing the ATSSS feature in practice means carrying out substantial and complex changes to many 5G network functions and supporting also non-3GPP interworking functions and the associated procedures in the UE for communicating with these functions.
MNO may not support N3IWF or TNGF uniformly in the whole PLMN and there can be scenarios, when N3IWF/TNGF is not available which may require a complementary solution which doesn’t require any 5GC support feature.
In addition, the placement of N3IWF/ TNGF (per TA or per whole PLMN) may provide limitations towards the performance of edge/critical services utilizing multiple access.
Observation 4: For such cases, the AL-ATSSS can be investigated so as not to require the deployment of extra functionality in core network.

## Slide 7: Proposed Study on Application support for ATSSS
The proposal targets to investigate a complementary ATSSS solution for vertical service enablement, which can be transparent to 3GPP core network where:
  The proxy functionality can be outside the UPF (in an enabler server/AF),
  The configuration and provisioning of the rules are for multi-access application sessions (in an enabler server/AF)
  It does not require N3IWF/TNGF/ePDG
  It can be tailored to support the requirements of verticals (e.g., steering rules may be provided by the verticals themselves)
  It can provide support for multiple 3GPP and non-3GPP access paths
  *It can be used to support existing (SEAL LMS) or Rel-19 proposed enablers (e.g. AEXR) utilizing both 3gpp and non-3gpp access paths.
*This study is not overlapping with the expected AEXR SID as well as the expected SEAL-Non-3GPP TEI, but rather complementary since it provides support for ATSSS rules configuration and provisioning over 3gpp and non-3gpp access.

## Slide 8: Potential objectives
The objectives of the study are to:
Analyze the SA1 Rel-19 requirements of DualSteer, as well as possible application layer impacts related to the Access Traffic Steering, Switching, Splitting (ATSSS) existing work in SA2.
Evaluate the need for an overall application framework/enabling layer architecture and associated requirements to support application-layer ATSSS (AL-ATSSS) for application sessions over multiple access networks (3gpp and non-3gpp);
Study architectural and functional implications on existing application enablers (e.g. SEAL, SEALDD) for supporting AL-ATSSS architecture;
Identify key issues based on 1), 2) and 3), develop corresponding functional model and potential solutions (e.g. discovery, multi-access session establishment, application service continuity) to support the implementation of AL-ATSSS, including potential UE and network APIs; and
Investigate possible impacts of AL-ATSSS for different deployments and business models.
Study how the AL-ATSSS can be used to support existing (e.g. SEAL) and new SA6 enablers (e.g. AEXR) for providing multi-access enablement capabilities.

## Slide 9
Back-up

## Slide 10: Exemplary AL-ATSSS architecture
In this exemplary architecture, an ATSSS enabler capability will be studied (as new enabler or enhancement of existing ones); as well as possible issues and solutions arising by this new architecture.
Such architecture may include new SA6 logical functionality(-ies):
ATEC: An application-layer function on the UE side, which triggers the establishment of an AL-ATSSS session, receives steering rules and other configuration data, and then transmits data traffic over multiple access paths based on the received steering rules.
ATES: An application-layer function on the network side, which may include an ATSSS Configuration Server (ATCS) functionality and an ATSSS Proxy Server (ATPS) functionality.
  The ATCS supports the establishment of AL-ATSSS Sessions requested by UEs (ATCEs) and the generation of steering rules and other configuration data for each AL-ATSSS session.
  The ATPS handles the user-plane aspects of an AL-ATSSS Session and forwards downlink data to ATEC via multiple access paths using the steering rules provided by ATCS.
Protocols like MPTCP, MPQUIC, etc. would be used in the ATEC and ATPS for handling communication over multiple access paths.
NOTE: A non-3GPP access path may or may not traverse 5GC

## Slide 11: Relation to existing enablers / SEALDD
SEALDD is a framework for supporting common data transport service capabilities such as data plane packet processing (e.g. packet duplication, elimination or transport coordination), data forwarding, data caching, background data transfer, etc. to support the VAL server and client.
SEALDD supports the session establishment for E2E redundant transmission, targeting only 3gpp access.
AL-ATSSS addresses from application-layer the need for a light ATSSS. The main points to cover are:
Study the need of a new capability of the ATSSS Configuration Server who allocates an ATSSS Proxy Server for an AL-ATSSS session, creates and distributes the UL/DL rules, provides measurement assistance information, etc.
Investigation of steering functionalities using MPTCP and MPQUIC that could be supported in the UE (ATEC) and in the ATSSS Proxy Server. Essentially, many of the concepts defined in SA2 ATSSS/Rel-18 could be applied in the application layer too.
Relevance to SEALDD:
The only relevance with SEALDD is that the ATPS can be deployed as a new capability of the SEALDD server and in this case the WID will provide enhancements to TS 23.433 too.
Why this shall be not part of SEALDD Ph2 SID proposal?:
It may not be the case that ATPS is deployed at SEALDD but could be also deployed as new enabler or at other vertical specific enablers / edge enabler / gateways (this will be the outcome of the study)
SEALDD provides support for redundant E2E paths, however if we assume non-3gpp access (not traversing 5GC), this requires a holistic discussion on the implications for providing support for traffic splitting/switching/steering.
SEALDD_Ph2 may not be the right place to study this, since the configuration of rules and protocol aspects may not be at SEALDD layer. SEALDD may only be used as a server acting as an ATSSS Proxy; however, the configuration may be another enabler dedicated for ATSSS feature.

## Slide 12: Estimated TU Calculation
Meeting | FS_AL-ATSSS (SID) | AL-ATSSS (WID)
SA6#56 (Aug-23) | SID Proposal | 
SA6#57 (Oct-23) | 1 TU | 
SA6#58 (Nov-23) | 1 TU | 
SA6#59 (Feb-24) | 1 TU | 
SA6#60 (Apr-24) | 1 TU | Work item Proposal
SA6#61 (May-24) |  | 0.5 TU
SA6#62 (Aug-24) |  | 0.5 TU
SA6#63 (Oct-24) |  | 0.5 TU
SA6#64 (Nov24) |  | 0.5 TU
Total | 4 TUs | 2 TUs