## Slide 1: Discussion on new WID SEALDD_Ph2
Cuili Ge, Jian Zhang
Huawei, Hisilicon

## Slide 2: Outline
Overall Justification
Possible objective
Background and motivation for Rel-19 new
Rel-18 leftover
Rel-19 new
SEALDD enabled Packet control
E2E measurement and optimization enhancement
Other information

## Slide 3: Overall Justification
Rel-18 leftover:
Due to the limitation of Rel-18 time-window and progress of SA2, there are some issues being identified but not concluded. The following aspects could be further studied:
the lossless data delivery enhancement
the possible architecture enhancement concerning the relationship with NRM server, the interaction of SEALDD-C interface
N6 header encapsulation for traffic information provisioning

## Slide 4: Overall Justification
Rel-19 new enhancement:
Packet control based on the Rel18 network capability/information exposures
Furthermore, multiple network capability/information exposures are newly introduced by SA2 in Rel-18, e.g., ECN marking for L4S, BAT offset. Though they are originated from XR, URLLC topics, they still can be potentially benefit other services for the data delivery with packet control. The SEALDD needs to adapt e.g., the packet transmission rate, next packet sending time to the network conditions reflected by the above networking information. How to coordinate the VAL server and SEALDD client over SEALDD-S and SEALDD-UU interface, to achieve the packet control is needed to be considered.
Enhancement to the transmission optimization based on the extended transmission quality results
Extending the E2E measurement from latency only to more KPI(s) is another aspect for Rel-19 SEALDD study. Based on Rel-18, SEALDD layer maintains the E2E connection and obtains the E2E transmission measurement (i.e., E2E latency). How to extend the E2E transmission measurement for more KPIs (e.g. jitter, congestion, etc), and the corresponding transmission optimization is critical to improve the VAL application performance.

## Slide 5: Possible Objectives
Description:
- Support the packet transmission control (e.g., rate adaptation, packet sending time) to improve the network performance and VAL application experience, by considering the network information (e.g. ECN marking for L4S, BAT offset, etc) exposed from 5GS.
- Extend the E2E transmission measurement to obtain more KPIs (e.g. jitter, congestion, etc), and develop the transmission quality optimization mechanism based on the KPIs and/or the network information exposed from 5GS.
- Enhance the existing lossless data delivery mechanism to enable corresponding interaction between the SEAL DD server and VAL server (e.g. the connection management and the context synchronization between SEALDD server and VAL server to ensure lossless transmission).
- The potential enhancements to the SEALDD architecture (e.g. the relationship with NRM server, develop SEALDD-C interface between VAL client and SEALDD client).
- Supporting SEALDD enabled N6 header encapsulation for traffic information provisioning to 5GC to improve the transmission performance and further enhancement.
NOTE: Coordination (e.g., N6 header encapsulation) with SA2 will be required.

## Slide 6: Rel19 new: SEALDD enabled Packet control
Scenario#1: Congestion control (ECN marking for L4S)
RAN
UPF
UE
DN
App client
App server
1. RAN or UPF performs ECN marking
2. L4S feedback
3. Rate adjustment for downlink direction
The required application requirements/dependencies:
- The application layer needs to support the ECN identify, ECN/L4S feedback
- The application layer performs data rate adjustment to reduce network congestion, and improve the application experience
Possible objectives in SEALDD:
- How SEALDD layer supports the ECN marking for L4S to offload the ECN processing at VAL application to simplify the application development
- How SEALDD layer performs the rate adjustment/adaptation for multiple VAL application, e.g. interacting with VAL server by enhancing the SEALDD-S interface

## Slide 7: Rel19 new: SEALDD enabled Packet control
Scenario#2: Application layer supporting of BAT offset
RAN
5GC
AF/AS
TSCAI (BAT adaptation capability, BAT window)
RAN determines the BAT offset
BAT offset feedback
Proactive RAN feedback
RAN
5GC
AF/AS
Packet arrive
RAN check whether AN PDB satisfies, and determines the BAT offset
BAT offset feedback
Reactive RAN feedback
The required application requirements/dependencies:
- The application layer needs to support BAT adaptation capability, and provide the BAT information
- The application layer needs to perform application-layer scheduling (e.g. adjust the packet sending time)
Possible objectives in SEALDD:
- How SEALDD layer supports BAT adaption capability to achieve application-layer scheduling?
- How SEALDD layer performs the packet control (e.g. adjust the packet sending time) considering the packet generation, packet collection, packet delivery over SEALDD-S and SEALDD-UU interface.

## Slide 8: Rel19 new: E2E measurement and optimization enhancement
In Rel-18, the SEALDD layer provides the E2E delay measurement , based on the time recording in packet sending/receiving
Possible objective in SEALDD:
- How to develop the transmission quality measurements mechanism to support more end-to-end KPIs (e.g. jitter, congestion, etc).
- How to extend the transmission quality optimization based on the transmission measurement results and/or the exposed network information.

## Slide 9: Other information
Continuation or New Item: SEALDD_Ph2
Study Item/Work Item/Both: WID
Source of requirements: SA2
Expected Output: content to be added to existing TS (23.433)
Anticipated start date/meeting: SA6#57
Target Completion: SA6#64
Estimated TUs: 8 TUs (WID)
Rapporteurship: Cuili Ge, Huawei
Supporting IMs:
Huawei
HiSilicon
CATT
China Unicom
China Telecom
TD Tech
ZTE
Vivo
Kyonggi University

## Slide 10: Other information
Dependency on other working groups:
- SA2
Impacts to 3GPP/Industry work if this is not accepted into Rel-19:
- lossless data delivery enhancement can not well serve the verticals.
- Lack of instruction of how SEALDD is well worked together with other SA6 tools (e.g., NRM).
- Vertical may not be able to use the new network capabilities due to lack of network acknowledge
- New network capabilities may not be well enabled without the AF/AS supporting