## Slide 1: Discussion on the reply to SA2 reply in S6-232240
Cuili Ge
Huawei, Hisilicon

## Slide 2: Background
Questions to SA6 from SA2
“To address SA6’s concern of potential packet loss, SA2 discussed different options to avoid packet loss for multicast MBS session used for mission critical service. Among the options, the option of MB-UPF buffering DL MBS data may have implication on latency of first packet(s) transmission, with further clarification as described in NOTE 8 in Table 5.7.4-1 of TS 23.501, therefore SA2 would like to check with SA6 whether there is concern on the latency of first packet(s) transmission resulted by the MB-UPF buffering and what the latency requirement of first packet(s) transmission for mission critical service is.”
Two questions:
whether there is concern on the latency of first packet(s) transmission resulted by the MB-UPF buffering
what the latency requirement of first packet(s) transmission for mission critical service is

## Slide 3: What SA6 can provide
SA6 has NO capability to evaluate the latency caused by the MB-UPF buffering
SA6 can only provide our requirements
KPI requirement
The MCPTT Access time(KPI 1) is defined as the time between when an MCPTT User request to speak (normally by pressing the MCPTT control on the MCPTT UE) and when this user gets a signal to start speaking.
The End-to-end MCPTT Access time (KPI 2) is defined as the time between when an MCPTT User requests to speak (normally by pressing the MCPTT control on the MCPTT UE) and when this user gets a signal to start speaking, including MCPTT call establishment (if applicable) and possibly acknowledgement from first receiving user before voice can be transmitted.
The Mouth-to-ear latency (KPI 3) is the time between an utterance by the transmitting user, and the playback of the utterance at the receiving user's speaker.
KPI 1 | MCPTT Access time | < 300 ms
KPI 2 | End-to-end MCPTT Access time | < 1000 ms
KPI 3 | Mouth-to-ear latency | < 300 ms
Requirement of audio lost
[R-6.15.3.2-016] There shall be no (0 ms) initial lost audio at receiving user.
UL T0~T1:150ms
DL T1~T2:150ms
Assume UL/DL is the same latency
UL T2~T3:150ms
DL T3~T4:150ms
SA6 can provide the requirements:
Month-to-Ear latency i.e., between an utterance by the transmitting user, and the playback of the utterance at the receiving user's speaker is 300ms and the receiving user may be in IDLE state when the transmitting user starts uttering.
There shall be no (0 ms) initial lost audio at receiving user.