## Slide 1: Discussion on media delivery functionality in SEALDD
Jian Zhang
Huawei, Hisilicon

## Slide 2: Outline
Background
Media delivery overview in SA4
Media delivery relationship between SEALDD and SA4
Summary and way forward

## Slide 3: Background
The SEALDD layer provides a general functionality to support data storage and data delivery by introducing 5G interaction (N5/N33 in control plane, N6 in user plane), including：
  Application data storage and management
  Application signaling and data transmission
  E2E URLCC transmission
  IoT message transmission (i.e. MSGin5G)
SEALDD architecture (TS 23.433)
As a general data delivery enabler, SEALDD should support the data transmission for all traffic types, including media type (e.g. media streaming, real-time media), this discussion paper mainly focuses on the following issues :
  The architecture relationship between SEALDD and SA4 in media communication
  The specific component of SEALDD compared with media functionality defined in SA4

## Slide 4: Media delivery overview in SA4
5GMS Application Provider supports：
  Media creation, media encoding, media formatting
5GMS AF supports：
  initiate or relay a request for different Policy or Charging Function (PCF) treatment or interact with other network functions via the NEF
5GMS AS supports：
  Ingesting media content from a 5GMSd Application Provider
  Caching media content to reduce the need to ingest the same content
  Adaptive Bit Rate (ABR) Encoding, Encryption and Encapsulation
  Geographic restrictions on content access by the Media Player
5GMS Provisioning
5GMS
Ingestion
Media streaming
Media session handling
Architecture#1: General Media streaming (MS) architecture (TS 26.501)
5GMS architecture defines the following APIs：
  5GMS provisioning API over M1 interface
  5GMS ingestion API over M2 interface
  Media session handling over M5 interface
  Media streaming over M4 interface
Notes: 补充Interface定义方面，

## Slide 5: Media delivery overview in SA4
RTC AF is dedicated to the real-time media communication, supports:
  Provisioning function with QoS support, QoE collection, etc.
  Configuration function with media configuration recommendation, etc.
  Network supporting function with QoS request
RTC AS is application server for the real-time media type, including:
  Signalling function manages media flow sessions in both uplink and downlink directions
  Content server that serves content to the WebRTC application
  Performs some media processing function such as transcoding, recording, 3D reconstruction, etc.
Architecture#2: General real-time communication (RTC) architecture (TS 26.506)
The 5GMS architecture and RTC architecture defined in SA4, is a general functionality to support media communication for media streaming application and WebRTC application, but how to use the specific optimization for XR application provided by 5G network is not involved, such as policy and media feature provisioning, application operation for the exposed network information, etc.
RTC architecture has the same principles of functionality classification as 5GMS architecture, but with the different protocols (e.g. RTP, RTCP)

## Slide 6: Media delivery relationship between SEALDD and SA4
VAL client(s)/5GMS or RTC aware application
media session handler
media player/framework
SEALDD client
Transmission adaptation over 5G
SEALDD-C
3GPP network system
5GMS/RTC AF
5GMS/RTC AS
SEALDD server
Transmission adaptation over 5G
N33/N5
N6
SEALDD-UU
VAL server(s)/5GMS or RTC application provider
SEALDD-S
VAL-UU
VAL UE
The SEALDD architecture for media delivery
The SEALDD as a general data delivery enabler, the following principles is utilized when supporting media type:
  The functionality/protocol defined in SA4 can be reused and further enhanced by SEALDD for supporting media type traffic
    The 5G transmission adaptation component is added in SEALDD, to facilitate the specific optimization for XR application provided by 5G network

## Slide 7: Proposal
The SEALDD mapping architecture as captured in slide 6 and the related CR (S6-23XXXX), should be agreed to support media type traffic.
Notes: Mapping关系slide6对应CR被agreed