## Slide 1: Discussion on virtual number capability provided by SA6
Yue Liu
China Mobile

## Slide 2: Examples of call related capabilities in the market
 | Huawei | Alibaba | Tencent | Vonage
Messaging | messaging and SMS | SMS | SMS | Messaging
virtual number | virtual number /private number | virtual number /private number |  | 
Voice calling | Voice calling | Voice calling | real time audio/video TRTC | Voice API
Verify number | Simple Message Notification | Verify Mobile number | Verify Mobile number | 
Voice messaging |  |  | Voice messaging | 
Contact Center |  |  | Cloud Contact Center | Conversation API
design flows |  |  |  | design flows across messaging and voice channels for chatbots or voice assistants
meeting |  |  |  | Meetings API
The capabilities listed below are some examples of call related capabilities in the market

## Slide 3: SA6 may provide some more value added service other than integration of SA2 APIs
SA6 can always integrate the capabilities provided by SA2 and re-exposes the capabilities in service level
Compared with capabilities provided in the market and eMMTel
  Voice calling is provided by SA2 and can be re-exposed by SA6
  virtual number is a very popular feature in market especially in China. It is proposed to support this feature in eMMTelAPP.
  Verify number is partly covered by KI#4 and related Solution#10,11,12,13 in SA2 TR23.700-77 (third-party identities). This feature is also partly included in KI#4 of SA6 TR23.700-92 (Application information)
  Messaging, Voice messaging and design flows are out of scope
  Whether meeting capabilities are needed is FFS.
  Other value added services are FFS.

## Slide 4: Use cases of virtual number (1)
virtual number looks like a real phone number rather than an anonymous number. This is a service level feature that cannot be handled in IMS/5GC. Some scenarios ( This is not an exhaustive list) are listed below.
AX
mode:
When user a1 requests to use virtual number, it may be assigned a virtual number x1.
When other users call x1, the call will go to a1.
When a1 calls other users, other users will see the caller number is x1
AXB mode:
The virtual numbers are depended on caller-callee pair.
When a1 wants to call b1 or a2 wants to call b2 and virtual number is requested to be used, a virtual number x1 can be assigned.
When a1 calls b1 or a2 calls b2, b1 or b2 will see the caller number is x1, but when other user calls x1, the call cannot go to either a1 or a2.
When a1 wants to all different users b1, b2 or b3, it should be assigned different virtual number x1, x2 and x3

## Slide 5: Use cases of virtual number (2)
XB
mode:
An enterprise has multiple employees can share a same virtual number x1 in different time.
AXE mode:
An enterprise has multiple employees can share a same virtual number x1 with different Extension.
AXYB
mode:
When user a1 requests to use virtual number, it may be assigned a virtual number x1.
Virtual number y1 and y2 are assigned to b1 and b2 respectively.
When other users call x1, the call will go to a1.
When a1 calls b1 or b2, it uses y1 or y2 respectively.
From a1 point of view, the callee is y1 or y2. From b1 and b2 point of view, the callee is x1.

## Slide 6: Proposals
It is recommend to include virtual number capability in eMMTel Enabler since it is a common capability especially in A2P scenarios.
Virtual number is a service level feature and cannot be handled in IMS/5GC.
Other common capabilities provided by eMMTel Enabler are FFS.