## Slide 1: Discussion on XR application server deployment enhancement
Huawei, Hisilicon
Yajie

## Slide 2
DNAI clarification
DNAI definition: Identifier of a user plane access to one or more DN(s) where applications are deployed.
Consider that multiple UPF may be deployed in one DN, thus one DNAI may used for identify multiple UPF
DN#1
DN#2
UPF#1
UPF#2
UPF#3
UPF#4
External router
DNAI#1

## Slide 3
Scenario clarification
Deployment: UPF#1 and APP server#1 are co-deployed; UPF#2 and APP server#2 are co-deployed
  User plane path#1 (UPF#1– APP server#1)：the internal router is used for transferring the data
  User plane path#2 (UPF#1– APP server#2) ：the network adapter is used for transferring the data
  The network adapter delay is shorter than internal router delay in current deployment
UPF#1
Internal router
APP
Server#2
User plane path#1 between UPF#1 and APP server#1
User plane path#2 between UPF#1 and APP server#2
RAN –UPF#1– APP server#1
External router
DNAI#1
Network adapter
UPF#2
APP
Server#1
RAN –UPF#1– APP server#2

## Slide 4
Issues on UPF and Application co-deployment
Currently, the UPF and application server selection is based on the DNAI information, which is not optimal mechanism, the reason is as follows:
Due to one DNAI may be mapped to multiple UPF:
  Only using DNAI for UPF and APP server selection, then the UPF#1 and APP server#2 may be selected for UE,
  In this case, the N6 delay still contains the delay of UPF#1 – APP server#2 (via Router(s)), and the delay may be longer than the delay of UPF#1 – APP server#1 which data transmitted only by network adapter
UPF#1
Internal router
APP
Server#2
User plane path#1 between UPF#1 and APP server#1
User plane path#2 between UPF#1 and APP server#2
RAN –UPF#1– APP server#1
External router
DNAI#1
Network adapter
UPF#2
APP
Server#1
RAN –UPF#1– APP server#2

## Slide 5
Potential way forward
Need to provide a mechanism to ensure the co-deployed UPF and APP server could be selected to further shorten the N6 delay
UPF#1
Internal router
APP
Server#2
User plane path#1 between UPF#1 and APP server#1
RAN –UPF#1– APP server#1
External router
DNAI#1
Network adapter
UPF#2
APP
Server#1

## Slide 6: The end